## Slide 1: Suomi NPP Status Jim Gleason NPP Project Scientist May 7, 2012
1
Launch: Oct 28, 2011

## Slide 2: Suomi NPP/VIIRS Instrument Status and Science Results”
Jim Gleason
NPP Project Scientist
JPSS VIIRS Operational Algorithm Team
VIIRS SDR
Changyoung Cao/NOAA/STAR
Frank DeLuccia/Aerospace
Jack Xiong/NASA
Robert Wolfe/NASA (Geo)
VIIRS EDR
Lead: Ivan Csiszar/NOAA/STAR
Clouds: A. Heidinger/NOAA/STAR
Ocean Color: W. Wang/NOAA/STAR
SST: S. Ignatov/NOAA/STAR
Imagery: D. Hilger/NOAA/STAR
Aerosol: I. Laszlo /NOAA/STAR
Land: I. Csiszar/NOAA/STAR
Cryo: J. Key/NOAA/STAR

## Slide 3
NPP with 5 instruments
VIIRS
CrIS
OMPS
CERES
ATMS
13.2 ft long
8.5 ft wide
4,500 lbs

## Slide 4: NPP Status
Spacecraft in normal Mission Mode, all systems nominal
Ground System performance nominal with data flowing to NESDIS and AFWA Centrals and to CLASS archive
All Instruments are in normal operational mode
  ATMS SDR data declared provisional (ready for broader use)
  ATMS SDR/TDR to be used operationally by NOAA NCEP in Spring of 2012
  VIIRS, CrIS, OMPS SDRSs have reached beta status
    Public Access through NOAA CLASS
  Product Validation work ongoing.

## Slide 5: Advanced Technology Microwave Sounder Northrop Grumman Electronic Systems
Description
Purpose: In conjunction with CrIS, global observations of temperature and moisture profiles at high temporal resolution (~ daily).
Approach: Scanning passive microwave radiometer
22 channels 23GHz - 183GHz
Swath width: 2300 km
ATMS SDR ready for Provisionally Release
ATMS data to be used by
NCEP Spring 2012
Departure; All Obs over Sea (K)
Satellite Zenith Angle (degrees)
ATMS has much better scan-dependent bias and (after re-mapping) noise levels are equivalent
AMSU-A vs ATMS Stats

## Slide 6
CrIS
Temperature
CrIS
Humidity
CrIS Data and Retreivals for 20 Jan 2012, t1910005
Single profiles
Notes: On behalf of the NPP/JPSS NOAA Cal/Val team, the first global dataset from CrIS was produced on Jan 20, 2012. Attached are four figures. The first is imagery from a single CrIS channel out of more than the 3000 channels that CrIS can generate. Each channel is sensitive to a different part of the atmosphere as well as the surface. The channel shown in this figure is a “window” channel at 900 cm-1 wavenumber (or 11.1 microns) and is very sensitive to the Earth’s surface and clouds. The second figure in the lower left is the spectrum of the myriad of CrIS channels in temperature units. The spectrum is used to derive the vertical temperature and moisture (humidity) information needed by the National Weather Service to forecast weather, both calm and severe, up to 5 to 7 days in advance. The figures to the right show the first temperature and humidity soundings generated by CrIS using a research algorithm developed by Dr. Bill Smith Sr.. It is fitting that Bill provided the first sounding, since Bill was a long-time friend and colleague of Professor Vern Soumi. Bill started his career at NOAA in 1965 and is a pioneer in the profiling of the atmosphere from Earth remote sensing satellites and continues to remain very active in the sounding research community.

## Slide 7: NPP CrIS Instrument Status
Exelis successfully performed Early CrIS instrument checkout and tuning from 1/28/12 to 2/21/12
Initial analysis shows that the instrument performance reaches and exceeds the pre-launch TVAC performance and specifications
Calibration coefficient table (Engineering Packet) version 32 was uploaded to CrIS instrument on 1/31/12, which includes update of some calibration coefficients determined from on-orbit data
Good Science RDR data started flowing from GRAVITE to the users on 1/20/12
Full spectral resolution data collection was performed successfully on 2/22/12 and 2/23/12
NEdN On-Orbit Data is Consistent with Ground Test Data (Black Lines); Much Better Than Spec Limits (Dashed Lines); Performance is Excellent. The relatively poor performance of MW FOV 7 (Middle green curve) was noted during ground testing and understood.

## Slide 8: CERES Flight Model 5 Regular Operations: January 24, 2012
CERES scanning radiometer measuring three spectral bands at TOA
  Total (0.3 to >50 m)
  Shortwave (0.3 to 5.0 m)
  Longwave Bandpass (8 to 12 m)
Operations, Data Processing, Products, and Science are a continuation of experience developed on
  TRMM (1), EOS Terra (2), EOS Aqua (2)
Reflected Solar Energy
Emitted Thermal Energy

## Slide 9: NPP Instrument Status: OMPS Nadir and Limb
Thirty Years of January 19th ozone

## Slide 10: NPP Instrument Status: VIIRS SDR (1)
All band are producing excellent images with expected quality
All onboard calibrators (BB, SD, SDSM) are functioning normally, providing good quality data for SDR calibration
  Reflective Solar Band (RSB) LUT have been successfully updated on-orbit;
  VIIRS SDR Inter-comparisons show good agreement with Aqua/MODIS after the LUT updates
  Thermal Emissive Bands (TEB) response is stable, and consistent with pre-launch analysis

## Slide 11: NPP Instrument Status: VIIRS SDR (2)
  Noise (NEdT) meets the sensor requirements for all detectors and all bands , consistent with pre-launch values;
  On-orbit calibration coefficients consistent with pre-launch values, except for M13 which is currently being updated
  Monitoring and trending shows all telemetry stable except the degradation in the NIR bands
  Geolocation LUT table was updated on 2/23, removed observed 1km offset
  An SDR Review meeting was held in April
  VIIRS SDR is in (de facto) beta status

## Slide 12: NPP Instrument Status: VIIRS Maneuvers
The following maneuvers have been performed successfully:
  Roll Lunar maneuver twice for RSB stability (1/4, 2/3)
  Yaw maneuver for SD and sun screen characterization (2/15-2/16)
  Pitch maneuver for TEB RVS characterization (2/20)
scan
track
scan
track
Pitch started at 18:15:34
Pitch ended at 18:59:19
Images of Band I5 SDR Brightness Temperature
Lunar Roll Maneuver
VIIRS Readout Timing modified for Lunar Rolls
Sector Rotation tested Feb 22, 2012
Response vs Scan Angle
M15 10.763 um
M16 12.013 um
300K
302K

## Slide 13: VIIRS M07 (0.865 microns) grey scaled 19 January 2012
VIIRS Data Anomaly
Degradation in M7/I2 observed after launch.
Smaller effect in M6 & M5.
Commissioning paused while anomaly was studied.
Degradation believed to be caused by an error in mirror coating process. An inadvertent layer of tungsten film was put on telescope mirrors.
Commissioning resumed Jan 18
Degradation is slowing, should level off.
No effect on VIIRS data products;
VIIRS SNR in M7 expected to be above spec.
Notes: The chart shows a map of the Global biosphere, land and ocean using SeaWiFS data. These data are used to monitor biological productivity. Changes in these data sets can be related to changes in how carbon moves through and is stored in the climate system and how the biosphere may be reacting to a changing climate.

## Slide 14: VIIRS Anomaly Change in VIIRS Solar Data as a function orbit number
F is conversion factor that compares the measured VIIRS solar data to the predicted value.
Data shows 1/F-factor. Should be 1 for new instrument.
Test periods used to diagnose VIIRS anomaly.
Data show anomaly depends on solar exposure; increases with light; stops in dark.
VIIRS 1394Anomaly
4 day Svalbard Line Outage –
Telescope rotating – slope looks unchanged
Door
Opened, Nov21
12/9 Test #1
Telescope stowed for 3 days
12/19 Test #2
Telescope night only
12/28 Test #3
Telescope stowed for 7 days
Jan 2 Test #4
Telescope stowed for 4 days
865 nm
746 nm
672 nm
Notes: On behalf of the NPP/JPSS NOAA Cal/Val team, the first global dataset from CrIS was produced on Jan 20, 2012. Attached are four figures. The first is imagery from a single CrIS channel out of more than the 3000 channels that CrIS can generate. Each channel is sensitive to a different part of the atmosphere as well as the surface. The channel shown in this figure is a “window” channel at 900 cm-1 wavenumber (or 11.1 microns) and is very sensitive to the Earth’s surface and clouds. The second figure in the lower left is the spectrum of the myriad of CrIS channels in temperature units. The spectrum is used to derive the vertical temperature and moisture (humidity) information needed by the National Weather Service to forecast weather, both calm and severe, up to 5 to 7 days in advance. The figures to the right show the first temperature and humidity soundings generated by CrIS using a research algorithm developed by Dr. Bill Smith Sr.. It is fitting that Bill provided the first sounding, since Bill was a long-time friend and colleague of Professor Vern Soumi. Bill started his career at NOAA in 1965 and is a pioneer in the profiling of the atmosphere from Earth remote sensing satellites and continues to remain very active in the sounding research community.

## Slide 15: #2 Witness Mirror Degradation with UV Exposure
SWIR Bands
VNIR Bands
M1
M7/I2
M6
M5
I1
M4
M3
M2
M8
M10/I3
M9
M11

## Slide 16
SWIR Turn-on shows
expected performance
Error Bars are +/-13% of predicted gain
  Original based sensor-TV, nominal plateau RC2 P2
  Degraded thruput reduces original by 24 hr UV exposure results for Witness#2

## Slide 17: VIIRS Anomaly Change in VIIRS Solar Data as a function of UV exposure
865 nm
746 nm
Anomaly depends on exposure to light, probably in the UltraViolet (UV) region.
Calculate amount of UV exposure in each orbit. Replot data, converting x-axis from orbit number to UV exposure time.
1 day UV exposure = 6.5 calendar days.
Data shows smooth dependence on UV exposure.
May 5, 2012
Notes: On behalf of the NPP/JPSS NOAA Cal/Val team, the first global dataset from CrIS was produced on Jan 20, 2012. Attached are four figures. The first is imagery from a single CrIS channel out of more than the 3000 channels that CrIS can generate. Each channel is sensitive to a different part of the atmosphere as well as the surface. The channel shown in this figure is a “window” channel at 900 cm-1 wavenumber (or 11.1 microns) and is very sensitive to the Earth’s surface and clouds. The second figure in the lower left is the spectrum of the myriad of CrIS channels in temperature units. The spectrum is used to derive the vertical temperature and moisture (humidity) information needed by the National Weather Service to forecast weather, both calm and severe, up to 5 to 7 days in advance. The figures to the right show the first temperature and humidity soundings generated by CrIS using a research algorithm developed by Dr. Bill Smith Sr.. It is fitting that Bill provided the first sounding, since Bill was a long-time friend and colleague of Professor Vern Soumi. Bill started his career at NOAA in 1965 and is a pioneer in the profiling of the atmosphere from Earth remote sensing satellites and continues to remain very active in the sounding research community.

## Slide 18: VIIRS Anomaly Conclusions VIIRS M07 (0.865 microns) grey scaled
Tungsten Mirror contamination identified as root cause. Limited to VIIRS FM1 mirror.
Continuing to Monitor degradation
Putting in weekly LUT updates
Testing time-dependent predictive LUTs
Bandpass effect (RSRs) studies ongoing
VIIRS SNR in M7 expected to be above spec.
For M7/I2 865 nm High Gain SNR
SNR Margin
Specification 215
Raytheon 419 95%
Notes: The chart shows a map of the Global biosphere, land and ocean using SeaWiFS data. These data are used to monitor biological productivity. Changes in these data sets can be related to changes in how carbon moves through and is stored in the climate system and how the biosphere may be reacting to a changing climate.

## Slide 19
Colorado
11.24.2011 1845 Z, Near Edge of Scan
11.24.2011 2028 UTC, Near Nadir
 VIIRS maintains similar spatial resolution quality at edge of 3000 km swath
NPP VIIRS True Color Examples
Notes: All examples use VIIRS global data sets kindly provided by either the U. of Wisconsin (CIMSS) via the NOAA IDPS or via the GRAVITE team effort.
This effort is a joint collaboration between the Naval Research Laboratory (NRL) Marine Meteorology Division, Monterey, CA and Dr. Steve Miller at the Cooperative Institute for Research in the Atmosphere (CIRA), located at Colorado State University (CSU) in Ft. Collins, CO.
This project is funded by the National Oceanic and Atmospheric Administration (NOAA), Joint Polar Satellite System (JPSS), Dr. Mitch Goldberg, Program Manager.

## Slide 20
Resolution Improvements: OLS vs. DNB
740 m instantaneous geometric field of view (DNB) vs. ~5 km for the OLS results in dramatic spatial resolution improvements.
DNB Imagery courtesy of Steven Miller CIRA/CSU

## Slide 21
Resolution Improvements: OLS vs. DNB
740 m instantaneous geometric field of view (DNB) vs. ~5 km for the OLS results in dramatic spatial resolution improvements.
DNB Imagery courtesy of Steven Miller CIRA/CSU

## Slide 22: Night Time Scene – Pakistan/India Border
Sodium Vapor lamps along Pakistan/India border show geolocation error of ~5 km to the east with Ops Geolocation
  Rev 001 DNB Geo LUT used for Jan 31, 2012 granule
  Highlighted region shown in detail on next slide
d20120131_t2128288_e2129530
S. Weiss, NGAS

## Slide 23: DNB Geolocation Improvement with LUT Revisions – Pakistan/India Border
DNB Geo LUT Rev 001
NGAS DNB Geo LUT Rev 003
DNB Geo LUT Rev 002
S. Weiss, NGAS
d20120131_t2128288_e2129530
Google Earth Border

## Slide 24: Geolocation Trending
375 m
Nadir equivalent units; Cross-correlation > 0.7; Outliers are filtered (removed) based on daily 5, 4 and then 3 sigma test
 | Bias (m) | RMSE (m)
Track | -20 | 89
Scan | -9 | 64
Error after LUT update (2/23/2012, doy 54)
41 days with average of 136 matchups/day (minus 11 outliers/day)
Feb. 23, 2012 LUT update

## Slide 25
VIIRS OC data compared with the MOBY in situ data, showing that SDR data since 2/6/2012 are good and reasonable, before that SDR date were poor/not reliable.
VIIRS ocean color products are good and reasonable from 2/6/2012.
Vicarious calibration is needed and will further improve ocean color products.
MOBY PI: Ken Voss
VIIRS vs. MOBY In Situ
Data from M. Wang
412
443
486
555
671

## Slide 26
Overall, deviation from reference flat & close to 0
Residual Cloud/Aerosol leakages in the Tropics
NIGHT: ACSPO minus OSTIA
‘Confidently Clear’ (No SST QFs are available in ACSPO)
Advanced Clear-Sky Processor for Oceans Operational Sea Surface Temperature and Sea Ice Analysis

## Slide 27
NIGHT: IDPS minus OSTIA
VCM = ‘Confidently clear’ (SST QFs are available but not used)
More Cloud leakages than in ACSPO (also in Hi Lat)
Some clear pixels screened out (e.g., Amazon basin)
“Limb Cooling” - Need recalculate SST coefficients

## Slide 28
ACSPO shows a large cloud-free domain
0.25° Reference SST fails to capture high local dynamics
ACSPO screens out large warm deviations from Ref
NIGHT: ACSPO “Confidently Clear” - Reynolds SST
Swath Projection: South-East Australia, 17 March 2012
1,000 Lines × 1,784 central FOVs (scan edges excluded to keep swath projection)

## Slide 29
IDPS VCM shows a much smaller cloud-free domain
“Salt-N-Pepper”, striping
..but preserves large warm deviations from Reference
NIGHT: IDPS “Confidently Clear” - Reynolds SST
Swath Projection: South-East Australia, 17 March 2012
1,000 Lines × 1,784 central FOVs (scan edges excluded to keep swath projection)

## Slide 30: Conclusions
Spacecraft in normal Mission Mode, all systems nominal
Ground System performance nominal with data flowing to NESDIS and AFWA Centrals and to CLASS archive
  Get VIIRS data from http://www.class.ngdc.noaa.gov/
  VIIRS SDRs available shortly (finishing README file)
  VIIRS Radiometry and Geolocation are good.
EDR Data Product Teams are busy.
  Tuning Cloud Mask
Contact JPSS EDR team leads for more details.

## Slide 31: Questions?
Fishing boats

## Slide 32
RTA Mirror Reflectance Degradation Anomaly
M8
M7
Reflectance degradation estimated using RTA primary mirror “TWM” witness sample measurements extrapolated to 4 mirrors by power law
1 mirror
2 mirrors
3 mirrors
4 mirrors
Degradation in the reflectance of the 4 RTA mirrors modulates VisNIR and SWIR RSR. Using NG Oct 2011 band averaged RSR, initial review suggests that radiometric impact <0.5%.

## Slide 33: NPP VIIRS At-Launch VisNIR RSR based upon preliminary Spacecraft Level RSR
In Process: update at-launch RSR with NG Oct 2011 RSR release, which is based upon final Govt. Team Spacecraft Level RSR.

## Slide 35
M bands
I bands

## Slide 36
4 mirrors degraded
M bands
I bands
(Percent)

## Slide 37
Over most ocean, the ΔTs field is flat and close to ~0
Residual Cloud/Aerosol leakages seen in the Tropics
Daytime positive anomalies – e.g., diurnal warming
DAY: ACSPO minus OSTIA
‘Confidently Clear’ (No SST QFs are available in ACSPO)

## Slide 38
Larger “CC” domain than in ACSPO, but..
Very significant Cloud leakages, all over
Some Limb cooling - Need recalculate SST coefficients
DAY: IDPS minus OSTIA
VCM = ‘Confidently clear’ (SST QFs are available but not used)

## Slide 39
MODIS
MODIS-Aqua, VIIRS (APS & IDPS)
Satellite Comparison
Ocean features, retrieved nLW and chlorophyll
have been shown to provide similar quality.
MODIS-Aqua
NPP- NRL processing
NPP- IDPS - VOCCO
Example: Feb. 28, 2012

## Slide 40
VIIRS products - Initial Evaluation
Feb 23, 2012 - Florida
Government Processing
MODIS vs NPP APS
VIIRS NRL -CHL
VIIRS NRL -412
MODIS Chl
MODIS -412
VIIRS Algorithms
IDPS vs APS
IDPS -412
APS -412
IDPS Chl
APS -Chlorophyll
Comparison of APS and IDPS products ?
MODIS vs IDPS –EDR’s
Feb 23 – 2012 – Florida
MODIS 412
MODIS Chlorophyll
IDPS VIIRS 412
IDPS VIIRS
VIIRS products compare with existing MODIS Products

## Slide 41
27th
28th
29th
1st
2nd
Walton Smith Cruise
Feb 28 – March 2 , 2012
Station Locations
Ondrusek, Goode, Wood
In situ Measurements
Above water measurement - ASD RRS,
In water measurement - HyperPro - Multicast
Waiting on the HPLC (Chlorophyll)

## Slide 42
MODIS
Florida
Keys
.01 .05 .3 1.6 8.4 45
mg/m3
MODIS NRL VIIRS IDPS VIIRS
Florida Florida Florida

## Slide 43
MERIS
NPP –VIIRS
– NRL 7g
L2gen
MODIS
Example:
Feb 28 , 2012
Inter–satellite comparison:
Backscattering
Particle at 551
IDPS
VOCCO

## Slide 44
MODIS vs IDPS –EDR’s
NPP - IDPS vs APS
Government Processing
MODIS vs NPP APS
VIIRS products - Initial Evaluation
2-28 , 2012 - Chesapeake Bay
MODIS 412
MODIS Chlorophyll
IDPS VIIRS 412
IDPS VIIRS
IDPS -412
IDPS Chl
APS -412
APS -CHL
VIIRS APS -CHL
VIIRS NRL -412
MODIS Chl
MODIS -412
2-28 , 2012 -
Chesapeake Bay

## Slide 45: VIIRS M05/M04/M03 (red/green/blue) VIIRS M15 (10.76 microns) color scaled from 225K to 325K 19 January 2012
Data processed at UW/SSEC as part of the NASA NPP Science Team

## Slide 46: NPP Science
Backup Material

## Slide 47
NPP VIIRS Pitch Maneuver on Feb 20, 2012, Orbit #1637
scan
track
GMT 18:22:02 – 18:27:44
Images of Band I5 SDR Brightness Temperature
GMT 18:47:39 – 18:53:20
4 granules at the beginning
4 granules near the end
Pitch started at 18:15:34
Pitch ended at 18:59:19
scan
track

## Slide 48: Brightness temperature profiles of pitch maneuver observed deep space for M15, M16 (no TEB RVS correction is applied)
Real deep space signals
Real deep space signals raised to Ltyp