## Slide 1: MODIS Sea-surface temperatures
Peter Minnett & BOB Evans
Rosenstiel School, University of Miami.
pminnett@rsmas.miami.edu

## Slide 2: Summary
MODIS SSTs are stable and of good accuracy
New algorithmic enhancements to improve accuracy, especially towards edges of swaths
New V6 code delivered to OBPG and tested for next reprocessing cycle
New M-AERIs being deployed for skin SST validation
SI-calibration traceability leads to rigorous CDR generation
  But desired CDR accuracies not yet met

## Slide 3: SST accuracy requirements
SST is an Essential Climate Variable (CEOS)
Required Errors and Uncertainties in SST for CDRs:
  Accuracy: better than 0.1K
  Stability: better than 0.04 K/decade
SST CDRs require traceability to SI-Standards
Difficulties are not only to achieve these, but to demonstrate whether they have been achieved
“Reference satellite sensor” – AATSR – terminated in April 2012 with failure of Envisat – focus on MODIS

## Slide 4: Atmospheric correction algorithms
Collection 5:
SST = a0 +a1T31 +a2(T31-T32) Tsfc +a3(sec(θ)-1)(T31-T32)
SST4 = a0 +a1T22 +a2(T22-T23) +a3(sec(θ)-1)
+ a4(fn(mirror.side)) +a5(θ) +a6(θ)2
+ a4(fn(mirror.side)) + a5(θ) +a6(θ)2
6:
Quality flagging improved

## Slide 5: Buoy matchups
Matchups between Aqua MODIS and drifters, after QA, for 2012. 79986 for day & night, but spatial distribution is uneven.
Buoy measurements are of a subsurface temperature.

## Slide 6: Terra Modis sst residuals
MODIS TERRA – SST residual statistics for each quality level (day + night) |  |  |  |  |  |  |  |  | 
Quality | Min | Q1 | Median | Mean | Q3 | Max | RMS | SD | MAD
0 | -4.461 | -0.359 | -0.109 | -0.110 | 0.137 | 6.080 | 0.453 | 0.439 | 0.368
1 | -5.170 | -0.574 | -0.209 | -0.244 | 0.114 | 10.851 | 0.715 | 0.672 | 0.507
2 | -7.573 | -1.457 | -0.779 | -1.040 | -0.283 | 5.525 | 1.598 | 1.214 | 0.833
MODIS TERRA – SST4 residual statistics for each quality level (night only) |  |  |  |  |  |  |  |  | 
Quality | Min | Q1 | Median | Mean | Q3 | Max | RMS | SD | MAD
0 | -4.475 | -0.292 | -0.140 | -0.163 | -0.007 | 4.664 | 0.359 | 0.320 | 0.210
1 | -4.756 | -0.474 | -0.223 | -0.283 | -0.027 | 4.703 | 0.529 | 0.447 | 0.324
2 | -6.673 | -1.071 | -0.411 | -0.641 | -0.057 | 3.765 | 1.102 | 0.896 | 0.660
Expect mean error of -0.17K from skin effect

## Slide 7: Aqua MODIS sst residuals
MODIS AQUA – SST residual statistics for each quality level (day + night) |  |  |  |  |  |  |  |  | 
Quality | Min | Q1 | Median | Mean | Q3 | Max | RMS | SD | MAD
0 | -4.546 | -0.362 | -0.131 | -0.139 | 0.093 | 13.024 | 0.460 | 0.438 | 0.338
1 | -5.882 | -0.565 | -0.208 | -0.255 | 0.087 | 10.948 | 0.701 | 0.652 | 0.477
2 | -7.231 | -1.584 | -0.851 | -1.111 | -0.323 | 8.764 | 1.639 | 1.202 | 0.885
MODIS AQUA – SST4 residual statistics for each quality level (night only) |  |  |  |  |  |  |  |  | 
Quality | Min | Q1 | Median | Mean | Q3 | Max | RMS | SD | MAD
0 | -4.394 | -0.312 | -0.152 | -0.183 | -0.013 | 3.961 | 0.385 | 0.339 | 0.219
1 | -5.178 | -0.597 | -0.292 | -0.381 | -0.074 | 3.473 | 0.640 | 0.514 | 0.372
2 | -7.684 | -1.871 | -1.041 | -1.235 | -0.348 | 4.111 | 1.703 | 1.172 | 1.101
Expect mean error of -0.17K from skin effect

## Slide 8: Median of SST errors
Terra
Aqua
Collection 5 – red. Collection 6 - blue

## Slide 9: Mean Abs Diffs of SST errors
Terra
Aqua
Collection 5 – red. Collection 6 - blue

## Slide 10: Comparison with other SSTs
Aqua MODIS SST vs Reynolds OI
Aqua MODIS SST vs WindSat SST

## Slide 11: Radiometers at Sea
Mean difference between M-AERI SSTs =0.064K

## Slide 12: M-AERI Calibration

## Slide 13: M-AERI deployments

## Slide 14: ISAR deployments

## Slide 15: MODIs – M-AERI skin SSTs

## Slide 16: Global Stats vs radiometers
MAERI | SST4 V6 |  |  |  |  | 
 | mean | median | sd | mad | IQR | N
TERRA | 0.047 | 0.082 | 0.297 | 0.227 | 0.291 | 84
AQUA | -0.056 | -0.024 | 0.304 | 0.242 | 0.308 | 135
MAERI | SST night V6 |  |  |  |  | 
 | mean | median | sd | mad | IQR | N
TERRA | -0.076 | -0.073 | 0.444 | 0.492 | 0.627 | 93
AQUA | -0.087 | -0.023 | 0.428 | 0.305 | 0.418 | 133
ISAR | SST4 V6 |  |  |  |  | 
 | mean | median | sd | mad | IQR | N
TERRA | 0.110 | 0.085 | 0.618 | 0.289 | 0.388 | 662
AQUA | -0.017 | 0.016 | 0.373 | 0.270 | 0.414 | 369
ISAR | SST night V6 |  |  |  |  | 
 | mean | median | sd | mad | IQR | N
TERRA | 0.003 | 0.044 | 0.716 | 0.525 | 0.727 | 798
AQUA | 0.059 | 0.066 | 0.495 | 0.384 | 0.521 | 355

## Slide 17: M-AERI Mk2
Three M-AERI Mk2s being deployed on RCCL cruise liners….

## Slide 18: M-AERI Mk3
M-AERI Mk 3 small
enough to be helicopter mounted….

## Slide 19: CDR generation

## Slide 20: Looking forward
Minor improvements to algorithms
Forward solution – optimum estimation of skin SST
Evaluate sampling errors resulting from clouds
Better partitioning of sources of uncertainties to derive improved estimate of MODIS SST accuracies
Continue at-sea deployments……
Continue to grow MUDBs to demonstrate stability of MODIS SSTs…
Ensure MODIS and VIIRS SSTs are compatible and can contribute to the SST CDR
Not seek the 8th significant figure in SST

## Slide 21: RSMAS SST TEam
Kay Kilpatrick
Gui Podesta
Miguel Izaguirre
Goshka Szczodrak
Liz Williams
Sue Walsh
Warner Baringer
Mike Reynolds – RMR Co, Seattle

## Slide 22: Summary
MODIS SSTs are stable and of good accuracy
New algorithmic enhancements to improve accuracy, especially towards edges of swaths
New V6 code delivered to OBPG and tested for next reprocessing cycle
New M-AERIs being deployed for skin SST validation
SI-calibration traceability leads to rigorous CDR generation
  But desired CDR accuracies not yet met…….