## Slide 1: NOAA/NCDC Surface Reflectance Climate Data Record Initiative
Eric Vermote(a), Chris Justice(b), Martin Claverie(b,a), Ivan Csiszar(c), Dave Meyer(d),Ranga Myneni(e), Frederic Baret(f), Ed Masuoka(a) , Robert Wolfe(a) and Sadashiva Devadiga(g,a)
(a)NASA/GSFC, Terrestrial Information Systems Branch, Code 619
(b)Department of Geography / University of Maryland at College Park
(c)NOAA/NESDIS/STAR
(d)USGS/EROS Data Center
(e) Dept of Geography and Environment, Boston University
(f) INRA/ Avignon, France
(g) SSAI
Contact: 301 6145413 eric.f.vermote@nasa.gov
MODIS/VIIRS Science Team Meeting, May 18 – May 22, 2015, Silver Spring, MD

## Slide 2
81
82
83
84
85
87
88
89
90
91
86
92
93
94
95
96
98
99
00
01
02
97
04
05
03
07
09
10
08
06
NPP
JPSS
11
AVHRR
VIIRS
Land Climate Data Record: Multi instrument/Multi sensor Science Quality Data Records used to quantify trends and changes
N07
N09
N11
N14
N16
N09
MODIS
Terra
Aqua
  AVHRR (GAC) 1982-1999 + 2001 (2003)-present
  MODIS (MO(Y)D09 CMG) 2000-present
  VIIRS 2011 – 2025
  SPOT VEGETATION 1999-2000
  Emphasis on data consistency – characterization rather than degrading/smoothing the data
VEGETATION
12
13
N18
14
15

## Slide 3
El Chichon
Pinatubo
Degradation in channel 1
(from Ocean observations)
Channel1/Channel2 ratio
(from Clouds observations)
BRDF CORRECTION
CALIBRATION
ATMOSPHERIC
CORRECTION
Land Climate Data Record
Needs to address calibration, atmospheric/BRDF correction issues

## Slide 4: Data products
CDR(s) | Period of Record and Temporal Resolution | Spatial Resolution & Projection Used (if applicable) | Update Frequency | Data file distinction criteria | Inputs | Uncertainty Estimates | Collateral Products
Surface reflectance (Red,NIR) NDVI | 1981-present daily | Linear Latitude Longitude (0.05deg) | daily | One file for each day and each CDR: Surface reflectance, NDVI | AVHRRGAC data | Reflectance (Red 0.02; NIR 0.03) NDVI (0.07) 3x3 average Reflectance (Red 0.01; NIR 0.015) NDVI (0.03) | LAI/FPAR

## Slide 5: Production Approach
Overview

## Slide 6: Production details
Geolocation
Calibration
95th AMS Annual meeting, Phoenix Arizona, January 4-8 2015

## Slide 7: Production details (cont.)
Atmospheric/BRDF correction
Cloud/Shadow screening
95th AMS Annual meeting, Phoenix Arizona, January 4-8 2015

## Slide 8: LAI/FAPAR Algorithm basis
The algorithm is based on a per-class neural network trained using AVHRR SR and MODIS LAI/FAPAR.

## Slide 9: Validation & Quality Assurance

## Slide 10
Assessing CLAVR using MODIS shows the need of an improved cloud mask
Evaluation of the global performance of the CLAVR Algorithm reported as percentage. Overall CLAVR identified only 2/3 of the cloud flagged by MODIS (red points), and labeled about 1/3 of the observation flagged as clear by MODIS as cloudy (blue points).

## Slide 11: Independent validation of MODIS internal cloud mask

## Slide 12
New improved cloud mask for AVHRR
Evaluation of the global performance of the LTDR cloud mask Algorithm reported as percentage.

## Slide 13: AVHRR Time series CLAVR mask

## Slide 14: AVHRR Time series LTDR cloud mask

## Slide 15: Methodology for evaluating the performance of surface reflectance product (generic)
Subsets of Level 1B data processed using the standard surface reflectance algorithm
Reference data set
Atmospherically corrected TOA reflectances derived from Level 1B subsets
Vector 6S
AERONET measurements
(τaer, H2O, particle distribution
Refractive indices,sphericityeri)
comparison

## Slide 16: Validation Metrics
Accuracy (A) = the bias
Precision (P) = the repeatability
Uncertainty (U) = the actual statistical deviation
From Vermote and Kotchenova, 2008
Specification (S) = Uncertainty requirement
S
Number of Occurrences
A, P, U, S
SR references

## Slide 17: MODIS SR validated over AERONET sites

## Slide 18: Using Direct comparison with MODIS Aqua for validation
Comparison of MODIS Aqua and NOAA16 AVHRR data, A (Red) ,B (NIR) ,C (NDVI) are observed over AERONET sites for 2003-2004, D (Red), E(NIR), F(NDVI) are simulated using a vegetation model that account for spectral difference between MODIS and AVHRR bands. G shows over the AERONET sites MODIS NDVI versus corrected AVHRR NDVI computed from spectrally adjusted AVHRR surface reflectance.

## Slide 19: Analysis of the AVHRR reflectance and NDVI time series reveal an issue with GAC sampling

## Slide 20: Analysis of the GAC artifact over AERONET SITES

## Slide 21: LAI Calibration procedure
We used the BELMANIP-2 sites network to calibrate the LAI/FAPAR ANN and the DIRECT in situ measurement to assess the uncertainty of the retrievals.
LAI
FAPAR

## Slide 22: Validation/Evaluation Results
Class | LAI |  |  | FAPAR |  | 
 | bias | RMSE | N | bias | RMSE | N
NeedleLeaf Forest | -0.04 | 0.31 | 2 |  |  | 0
BroadLeaf Forest | 0.39 | 1.18 | 22 | 0.07 | 0.15 | 5
Shrublands | 0.02 | 0.93 | 20 | 0.04 | 0.13 | 25
Grasslands & Croplands & Non vegetated | 0.11 | 0.69 | 51 | 0.05 | 0.16 | 40
evergreen broadleaf forest | -0.81 | 1.53 | 14 | -0.07 | 0.07 | 2
All | 0.13 | 1.05 | 171 | 0.05 | 0.15 | 72
In situ validation: we extrapolated DIRECT measurement (1km footprint) to 0.05degree using MODIS LAI/products
Product evaluation: inter-comparison of NOAA-16 vs NOAA-18 outputs

## Slide 23
Operational Quality Assurance

## Slide 24
Assessment of the impact of the 2012 Northern Hemisphere Drought from the MODIS Climate Modeling Grid daily NDVI data. The anomaly image shows the cropland NDVI departure from the average (2000-2011) on July 30th 2012, highlighting hotspots of crops under stress during the 2012 droughts that affected the United States and the Black Sea region. The time-series curves below compare the daily development of croplands in 2012 (red) to average (2000-2011) in 3 important crop growing regions: Illinois, USA; Orenburg Oblast, Russia; Kostanay Oblast, Kazakhstan. The crop development through the season depicted by NDVI shows consistent negative anomalies with regard to a ten year average, with highest discrepancies during the crops peak development period. In 2012 crops in the US, southern Europe and the Black Sea region suffered from prolonged high temperatures and lack of moisture, which resulted in significantly reduced production. This information was available one month prior to harvest and several months before the release of official statistics.
MODIS NDVI Anomaly July 30th 2012

## Slide 25: Prototype VIIRS NDVI Anomaly, July 30th 2012
A VIIRS NDVI anomaly (prototype) image computed for the same date (July, 30th 2012) as the MODIS NDVI anomaly shown in the previous slide, generated from data produced at the GSFC Land PEATE.

## Slide 26: Application to Agriculture: Yield/Production prediction
Kansas: Wheat
Ukraine: Wheat
Becker-Reshef, I., E. Vermote, M. Lindeman, and C. Justice (2010a), A generalized regression-based model for forecasting winter wheat yields in Kansas and Ukraine using MODIS data, Remote Sensing of Environment, 114(6), 1312-1323.

## Slide 27
ANDVI, GDD climatology
Daily accumulated Growing Degree day
(GDD)
Daily BRDF-corrected NDVI adjusted (ANDVI)
ANDVI, GDD
Adjusted NDVI and accumulated GDD for the day of the forecast
Wheat mask
Simulated adjusted peak NDVI (~ANDVIpeak)
Median ANDVI at the peak and at GDD of the day of forecast
(median based on 2000 to 2012 data )
Becker-Reshef et al. (2010) method
Inputs
Mpct
% Wheat in each Administrative Unit (AU)
Improving timeliness of winter wheat production forecast in United States of America, Ukraine and China using MODIS data and NCAR Growing Degree Day
Remote Sensing of the environment, 161,131-148 (2015)
B. Franch1,2, E. F. Vermote2, I. Becker-Reshef,1 M. Claverie1,2, J. Huang1, J. Zhang1, and J.A. Sobrino3
1 Department of Geographical Sciences, University of Maryland, College Park MD 20742, United States
2 NASA Goddard Space Flight Center, Code 619, 8800 Greenbelt Road, Greenbelt, MD 20771, USA
3 Global Change Unit, Image Processing Laboratory (UCG-IPL). Parque Cientifico, Universitat de Valencia, Spain

## Slide 28: Results for major producers
USA
Ukraine
China
The results show that the earliest time winter wheat production can be forecasted within an error of 10% is roughly one and a half month prior to the average date of the peak, that is two months and a half month prior to the harvest

## Slide 29
Percent tree cover, Amazon Basin, 1990--Land LTDR AVHRR data
funded MEASURES-2013 proposal entitled "Vegetation Continuous Fields ESDR for the AVHRR and MODIS Records: 1981 - Present", PI: Robert Sohlberg (UMD).

## Slide 30
Percent tree cover, Amazon Basin, 2000—MODIS CMG data

## Slide 31
Percent tree cover, Amazon Basin, 2010--MODIS CMG data