## Slide 1: Land SIPS: Data Formats and Software Updates
Carol Davidson
Science Systems and Applications, Inc.
Carol.C.Davidson@nasa.gov

## Slide 2: Operational Interface
LP-DAAC
NSIDC
Ocean SIPS
L1 code repository
Land SIPS
NASA VIIRS Land Science Team
NASA VCST and GEO
EDOS
L0 Processing
LDOPE
LAADS
Science Data L0 – L3/l4
L0 Data
Science Data
L0 Data
L1B and Geo Proc. code and LUT
Test Requests
Science Code Delivery
Science Test Requests
Recomm-
endations
Responses
Science Data
L1B and Geo Proc. code and LUT
L1A Proc. code

## Slide 3: Data Formats: L1
LSIPS is transitioning to the NASA VIIRS L1 Datasets:
  L1A
    Uses L0 PDS files supplied by EDOS
  Geolocation
  L1B
    Very different from SDRs
    More like MODIS L1B
    No Geolocation datasets, only GRing and BoundingCoordinate metadata attributes.
Data format: netCDF4.2/HDF5
  CF-1.6 Convention
6-minute Granules

## Slide 4: Data Formats: L2 Swath
Is your Swath data going to LP DAAC or NSIDC?
  YES:
    Data format: netCDF4.2/HDF5
    CF-1.6 Convention
    Meets metadata requirements defined by DAACs and LDOPE
    Needs metadata xml file as well for ingest at DAAC
  NO:
    Data format: SCF’s choice.
      HDF4 (for now)
      netCDF4.2/HDF5
    Meets metadata requirements needed for MODAPS/LAADS and LDOPE
All swath products are 6-minute granules

## Slide 5: Data Formats: Gridded Products
Is your L2G, L3 Daily L3 n-day or L3 CMG product going to LP DAAC or NSIDC?
  YES:
    Data format: HDF5-EOS
    Meets metadata requirements defined by DAACs and LDOPE
  NO:
    Data format: SCF’s choice.
      HDF4-EOS (for now)
      HDF5-EOS
    Meets metadata requirements needed for MODAPS/LAADS and LDOPE

## Slide 6: Software Updates Overview
SCF Obtains latest tagged version of code package*
New version of PGE submitted to CM for tagging, then onto Science Test if needed/requested.
LSIPS SSTG integrates, compiles and tests code package from SCF. Test results are shared with SCF as needed/requested to verify code integration.
SCF modifies and tests code changes and prepares updates for delivery to LSIPS SSTG.
SCF sends code package with test inputs/outputs to LSIPS SSTG Lead. Delivery notice via email to carol.c.davidson@nasa.gov with location and notes on package changes.
Prior to delivery, SCF compiles and executes on LSIPS development machine: npp1.
*If update to existing PGE.

## Slide 7: Software Updates
Detailed instructions for obtaining, updating, compiling, testing and delivering code changes are in the document:
Science Software Updates in the Land SIPS.docx
Instructions for obtaining access to the NASA machine are in the document:
AccountAccess_V3.docx
Contact LSIPS SSTG Lead for copies of both.

## Slide 8: Software Updates, additional notes
SDPToolkit In use for HDF library functions at LSIPS, but not the MODIS PGSToolkit
  PGSToolkit library functions need to be removed
LSIPS uses 64-bit machines
HDF5 functions in LSIPS OPS Libraries
  For reading in NASA VIIRS L1B and Geolocation
  Primarily supports IDPS heritage codes
  May be useful to others
Make sure your code is ready to work with correct input/output format
  netCDF4.2/HDF5 for L1s
  Mixed types for swath and gridded
    Double check format types with LSIPS SSTG

## Slide 9: LSIPS SSTG & Data Production Team
Science Software Transfer Group (SSTG) Development and Integration Team:
  Cid Praderas, cid.praderas@ssaihq.com
  Anhquan Nguyen, anhquan.d.nguyen@nasa.gov
  Virginia Kalb, virginia.l.kalb@nasa.gov
  James Kuyper, James.R.Kuyper@nasa.gov
  Maki Jackson, Maki.Jackson@gst.com
Data Production and Archive:
  Cynthia Hamilton, cynthia.m.hamilton@nasa.gov