## Slide 1: VIIRS Issues and Perspectives
Jim Gleason
Suomi Project Scientist
June 6, 2016
VIIRS Blue Marble Stamp
June 2016

## Slide 2: Suomi NPP Status
Suomi NPP Instrument Status
  CrIS, OMPS CERES; all nominal
  ATMS; known bearing degradation issue
    Change in con-ops; revealed FSW error
    Reverse motor direction once-per-day
  VIIRS; Nominal
    HAM-sync error; periodic short term (90s) loss of data
    SEU-caused computer lock-up aka petulant mode
      Std reset procedure (1-2 orbits lost)
    Tungsten-oxide mirror contamination
      Following thin-film model
      Will meet requirements at EOL

## Slide 3: JPSS Status
  JPSS-1 Launch: January 2016
  All Instruments Complete
  All Instruments Integrated on Spacecraft
  Observatory in Environmental Testing
    Currently in EMI/EMC testing
    Observatory T/V in July-September 2016
  J1 VIIRS is an excellent, well characterized instrument.
    Nine M-band waivers
    Two DNB waivers
    All performance data is available to interested parties

## Slide 4: J1 VIIRS Performance Waivers
The joint NASA/NOAA Performance Waiver WG discussed and deemed acceptable the following waivers on science performance:
  Spatial resolution – better than allowed by spec established after NPP
  Dynamic Range – several bands saturate before spec Lmax, similar to NPP but exacerbated by somewhat higher optical throughput achieved on J1
  Near-Field Response – better than NPP but worst-case contamination at end-of-life still violates spec requirements
  Crosstalk – much better than NPP but still non-compliant to the specification
  Band-to-Band registration – overall better than NPP, but different in details (VIIRS J1 misregistration largely in track vs. mix of scan and track on NPP)
  Emissive Band Radiometric Calibration – similar to NPP, concerns on J1 mostly have to do with response uniformity and the potential for striping
  Reflective band radiometric calibration – dominated by SWIR low radiance non-linearity (new for NPP) which could impact processing approaches
  Relative Spectral Response – similar to NPP, and T-SIRCUS at Raytheon
  Polarization – non-compliance not seen on NPP but acceptable on J1 based on more extensive characterization testing, modeling, and model validation
  DNB Stray Light – similar to NPP, mitigated by correction in ground system
  DNB non-linearity – new for NPP, non-compliant at low light levels in modes baselined for edge-of-scan. Mitigation for J1 substitutes compliant modes.

## Slide 5: JPSS -2,-3,-4
JPSS-2 VIIRS – Complete
Almost ready for ambient testing
Launch July 2021 (notional)
JPSS-3 VIIRS and JPSS-4 VIIRS
Raytheon under contract
No significant performance changes planned
JPSS-3: Launch Date July 2026 (notional)
JPSS-4: Launch Date July 2031 (notional)

## Slide 6: Ground System Updates
Level 0
New Data path for SNPP and JPSS data
EDOS network till Fall 2016
JSH in Suitland Fall 2016 – end of JPSS Program
EDOS L0 format
Level 1
NASA VIIRS L1 algorithm complete
L1A format for easier reprocessing

## Slide 7: SDS SNPP Data Acquisition (Operational)
SvalSat
Svalbard
FCDAS
Gilmore Creek
(contingency only)
Closed
EBnet
EDOS
HRDFEP
EDOS
HRDFEP
Sounder
CrIS/ATMS
CERES
NASA
SIPS
VIIRS
Atmosphere/
Land/Ocean
Ozone
OMPS
EDOS
LZPF
Open
EBnet
via DREN
at ASF
Internet 2
Level 0 NASA EDOS network
NASA EDOS format (not NOAA C3S/IDPS)
New Data path for SNPP and JPSS data till Block 2.0

## Slide 8
SDS Data Flow in Block 2.0
SNPP and JPSS
EDOS
formats
JSH
in Suitland
NOAA Networks
To Suitland

## Slide 9: Summary
SNPP VIIRS
Performance nominal
New L0 data path using known EDOS L0 format
NASA L1 algorithm complete
JPSS-1 VIIRS, Complete
JPSS-2 VIIRS, Assembly in progress, ready for test
JPSS-3,-4 VIIRS, Under contract
VIIRS data record begins in 2012 and will end beyond 2036
Opportunity for 40 year combined MODIS-VIIRS data sets

## Slide 10: Questions?

## Slide 11
S-NPP & JPSS-1 Mission Orbit View
(1325 LTAN/824 km orbit)
½ orbit along-track separation

## Slide 12: S-NPP & JPSS-1 Sensor Overlap (1325 LTAN/824 km orbit)
NPP
JPSS1 (not on map)
Sensor swath overlap
Spacecraft Follow Different Ground Tracks
Based On ½ Orbit Along-Track Separation

## Slide 13
SNPP
JPSS1 50 min lead
JPSS1 ½ orbit lead
Ground track path centers
Earth rotation
Order of equator crossing: JPSS1; JPSS1 45 seconds later; SNPP 50:45 later (1/2 orbit is ≈50:45)
JPSS1 and SNPP cross through center of ground track 8 paths apart.
JPSS1 crosses ≈21 km to the “west” of the center of the ground track
Ascending Node Crossing
JPSS-1 wrt S-NPP (1/2 orbit along-track separation)

## Slide 14: Questions?
Backup

## Slide 15: S-NPP & JPSS-1 with 5 instruments
VIIRS
CrIS
OMPS
CERES
ATMS
13.2 ft long
8.5 ft wide
4,500 lbs

## Slide 16: Suomi NPP VIIRS Degradation Analysis and Prediction
4-mirror thin-layer model
V15 data up to Dec 19, 2014
Ref: Lei, et al, SPIE Proceeding, Vol 8533, paper 19 (2012)
Lei, et al, IEEE Trans. Geosci. Remote Sens., Vol 53, pp 1565-1573, (2015)

## Slide 17: Suomi NPP VIIRS Degradation Analysis and Prediction
4-mirror thin-layer model
V15 data up to Dec 19, 2014
Ref: Lei, et al, SPIE Proceeding, Vol 8533, paper 19 (2012)
Lei, et al, IEEE Trans. Geosci. Remote Sens., Vol 53, pp 1565-1573, (2015)
I1
M5
M6
I2

## Slide 18: VIIRS Spectral Response Example; M1 412 nm
JPSS 1 VIIRS
Suomi NPP VIIRS

## Slide 19
JPSS-1
S-NPP
Svalbard
JPSS-1 Orbit and Constellation View
Snapshot taken at time when both
spacecraft above Svalbard horizon
(magenta colored circle)
JPSS-1
S-NPP
227 nodal crossings
13:30
LTAN
Cross different node at
same LTAN
Part of JPSS satellite constellation at 824 km and 1330 LTAN, polar sun-synchronous orbit
16 day repeat cycle like S-NPP
JPSS-1 leads S-NPP with a minimum of 20 min orbital separation
  Support instrument calibration using cross reference
  Avoid ground contact conflicts
  Working with GSFC A-train personnel and are preparing for meetings with JPSS Flight/LV to start coordination of mission orbit insertion

## Slide 20: Mission Orbit Constellation Concept
Current Timeframe
  Program Science was asked to review/revisit the constellation concept (December 2014 timeframe) and responded with request to evaluate ½ orbit along-track separation concept (based on Eumetsat EPS-SG concept)
  PSE coordinated study involving science/flight/ground/mission ops to assess feasibility and impacts for changing the along-track separation
Diagrams/pictures based on analysis performed by Richard McIntosh/Dave Rohrbaugh (a.i. solutions)
½ orbit along-track separation between JPSS-1 and S-NPP in the same mission orbit plane (824 km, 1325 LTAN)
Ground Track Diagram
Blue line/swath – JPSS-1; Yellow line/swath – S-NPP;
Grey swath – coverage overlap of JPSS-1 trailing edge with S-NPP leading edge; eliminates bow-tie effect

## Slide 21: JPSS-1 Orbit Paths for 16 Days
Orbit grid for JPSS1 (ascending node paths shown) – there are 227 orbit paths for every 16-day cycle

## Slide 22: JPSS-1 Orbit Paths
Map shows orbit paths for slightly more than one day to see how the ground track is laid out
Consecutive orbits track 16 paths apart
Orbit 1
Orbit 2
Orbit 3
Orbit 4
Orbit 5
Orbit 6
Orbit 7
Orbit 8
Orbit 9
Orbit 10
Orbit 11
Orbit 12
Orbit 13
Orbit 14
Orbit 15
Orbit 16

## Slide 23: S-NPP & JPSS-1 Ground Track (1325 LTAN/824 km orbit)
NPP
JPSS1
Equator
Spacecraft Follow Different Ground Tracks
Based On ½ Orbit Along-Track Separation

## Slide 24
176.542 km
Path 1
Path 2
Path 3
Path 4
SNPP
JPSS1
½ orbit
ahead
50:45 minute Earth Rotation
(1/2 SNPP orbit)
Path 5
Path 6
Path 7
Path 8
JPSS1
50 min
ahead
21 km
JPSS-1 wrt S-NPP (1/2 orbit along-track separation)
Note: Path numbers do not correspond to orbit numbers.