## Slide 1
Revealing changes in phytoplankton community structure with MODIS using an ocean reflectance inversion model
Jeremy Werdell 1, Collin Roesler 2, Joaquim Goes 3
Lachlan McKinna 1, Bryan Franz 1
1 NASA Goddard Space Flight Center
2 Bowdoin College
3 Lamont Doherty Earth Observatory
MODIS-Aqua image credit: Norman Kuring (GSFC) & the NASA Earth Observatory

## Slide 2: Remote-sensing of phytoplankton communities: A consumers’ market
http://www.ioccg.org/groups/PFT.html
http://ioccg.org/groups/PFT-TM_2015-217528_01-22-15.pdf

## Slide 3: New satellite missions sold with a promise of resolving phytoplankton community structure

## Slide 4: Two flavors of algorithms exist
abundance methods
assume a given phytoplankton biomass, defined by either Chl or absorption – covaries with the dominance of or fraction of a particular community
diatoms
cyanos
spectral methods
variations realized in the spectral shape of Rrs(l) or absorption vary with community structure
unlike abundance approaches, these can detect different communities with common total biomass, provided the groups have contrasting optical signatures
but, often confounded by variations of spectral characteristics of the same community due to growth conditions, nutrient availability, & ambient light regimes
0.95 ≤ Chl ≤ 1.05 mg m-3

## Slide 5: Ocean reflectance inversion algorithms (one spectral method)
terms with blue bars have pre-assigned spectral shapes associated with them (known or modeled)
find combination of M’s (red bars) such that right hand side best reconstructs left hand side
what the satellite sees
what we want to estimate
forward model inverse model

## Slide 6: Quick aside: Our MODIS work
Generalized Inherent Optical Property (GIOP) framework
Standard OBPG (community supported) software for deriving spectral absorption & scattering coefficients from MODIS, VIIRS, others
Default parameterization, but alternate configurations available at runtime
Learn more: Werdell et al. (2013a), Franz and Werdell (2010)
MODIS T&A award to enhance GIOP & develop improved spectral absorption & scattering coefficients
Seawater backscattering temp & salinity dependencies (Werdell et al. 2013b)
Iterative mode per Wang et al. 2005, Brando et al. 2012 (aLMI)
Configurable expanded solution space (e.g., Mph1 … MphN) (Werdell et al. 2014)
Configurable BRDF effects
Raman effects per Westberry et al. 2013, Lee et al. 2013 (McKinna et al. 2016)

## Slide 7: Resolving community structure using (spectral) inversion algorithms
A
B
1
2
3
4
5
6
7
8
9
10
11
12
13
7-13 March 2011
13-19 March 2011
a mixotrophic dinoflagellate
(green version)
(1) heterotrophy - feeds on bacteria, diatoms, copepod eggs, detritus, Trichodesmium (?)
(2) symbiosis – houses the photosynthetic, green flagellate Pedinomonas noctilucae
can the temporal & spatial evolutions of Noctiluca in the northern Arabian Sea be determined using satellite ocean color?

## Slide 8: Resolving community structure using (spectral) inversion algorithms
terms with blue bars have pre-assigned spectral shapes associated with them (known or modeled)
find combination of M’s (red bars) such that right hand side best reconstructs left hand side
what the satellite sees
what we want to estimate
forward model inverse model
MODIS l

## Slide 9: Tools & data sets
~1,500 viable simulations
~30 Hydrolight batch runs (sigh)

## Slide 10: Vertical structure & mixed communities are problems
0.5 mg m-3
1.25 mg m-3
average
0.95 mg m-3
optically
weighted
2 mg m-3
DCM
Chl values the satellite sees as the bloom deepens
Depth of the DCM (m)
Rrs(l) Rrs(l)
magnitude observed by satellite does not unequivocally inform about the vertical structure
how reliable & meaningful are the derived magnitudes in assigning community dominance?

## Slide 11: Vertical structure & mixed communities are problems
only diatoms ~0.5 mg m-3
only Noctiluca ~0.5 mg m-3
only diatoms ~1 mg m-3
only Noctiluca ~1 mg m-3
0.5 mg m-3 each (= 1 total)
some false positives for diatoms when only Noctiluca present
few false positives for Noctiluca when only diatoms present
separation of two in mixed communities less reliable
argues for more “binary” interpretation for presence or absence of Noctiluca
and, for cautious interpretation of estimated absolute magnitudes of retrievals

## Slide 12: Is it there or is it not?
satellite Chl
in situ Chl
diatoms
Noctiluca (>1 with diatoms < 0.3)
Noctiluca (previous condition not met)
total chlorophyll
diatom component
Noctiluca component
red is Noctiluca ID’ed

## Slide 13: Application to MODIS-Aqua time-series
Noctiluca seen in places not previously sampled
Noctiluca distributions not correlated to total Chl
Identified Noctiluca Chlorophyll

## Slide 14: Application to MODIS-Aqua time-series

## Slide 15: Lessons were learned
Ocean color inversion methods address ill-posed problems
Can successfully identify presence of a dominant species (with TLC, when assumed spectral shapes match reality)
Less successful providing information on vertical structure
Retrieved magnitudes require careful interpretation
Ocean color data records provide a highly useful tool in combination with other satellite & in situ assets
Reduces ambiguity in vertical structure & physiology
Additional spectral information provides additional insight
(Not shown) Validation remains challenging & other ocean color products (backscattering, fluorescence) can be useful
Do the right in situ data sets (and, instruments) exist?
Can these data sets be post-processed in such a way to reproduce the integrates values seen by the satellite?

## Slide 16
thank you

## Slide 17: March 2011 optical properties
adg(443)
bbp(443)
# of N. miliaris identified
bbp(443) / Chl

## Slide 18: Fluorescence
OC3 0.05 to 50 mg m-3
nFLH 0 to 0.04 mW cm-2 nm-1 sr-1

## Slide 19: Moving towards hyperspectral information
Derivative analyses
of Rrs(l) may reveal community composition based on differences in phytoplankton absorption
Legend:
Noctiluca only
Diatoms only
Both ~0.5 mg m-3
average spectra
all spectra
Second derivative Rrs(l) Second derivative Rrs(l)