## Slide 1
Volcano monitoring using MODIS
Robert Wright
Hawaiʻi Institute of Geophysics and Planetology, Honolulu, HI

## Slide 2
http://modis.higp.hawaii.edu

## Slide 5
MODIS has detected volcanic thermal anomalies at over
100 volcanoes since 2000

## Slide 6
Relatively insensitive to low temperature and hydrothermal volcanic
(i.e. non-eruptive) phenomena

## Slide 7
MODIS measurements of emitted spectral radiance act as an effective proxy of eruption intensity during volcanic eruptions
2006 eruption of Mount Augustine, Alaska
Source: USGS
Power et al., (2006)

## Slide 8
Some volcanoes have been persistently active since 2000

## Slide 9
Some volcanoes have erupted only once since 2000

## Slide 10
Some volcanoes have been episodically active since 2000

## Slide 11
MODIS has catalogued volcanic thermal emissions at the global scale
Mafic lava flows
Mafic lava lakes
Felsic lava domes
Vent activity
Carbonatite lavas

## Slide 12
Total energy radiated
Peak radiant flux
Allowing for direct quantitative comparisons of the intensities and magnitudes of terrestrial eruptions

## Slide 13
MODIS reveals evidence for periodicity in thermal output at some volcanoes, but not at others
Wright et al. 2015

## Slide 14
MODIS allows us to estimate the volumetric flux of lava from the vent
5 km
Integrating effusion rate over time allows the total lava output to be estimated, and MODIS-derived estimate of final volume (1.3 km3) is consistent with in-situ estimates (~1.2 km3)
Bonny, Thordarsson, and Wright, in review

## Slide 15
The rate at which (and total amount of) lava that is erupted constraints sub-surface magma chamber conditions

## Slide 16
Can we use MODIS data to predict when an eruption will end?

## Slide 17
Using MODIS data to predict when an eruption will end
Nyamuragira, Democratic Republic of Congo, 2000
Bonny and Wright, in review

## Slide 18
Using MODIS data to predict when an eruption will end
Kizimen, Russia, 2011

## Slide 19
No reason why MODIS cannot be used to predict lava flown hazards in near-real-time
Wright et al. 2008