## Slide 1
Atmo. C7, MODIS/VIIRS STM, May. 2023
MODIS Atmosphere Product Collection 7 (C7):
Summary of Plans/Status
1NASA GSFC, 2SSAI, 3GESTAR/UMBC, 4ORAU, 5U. Wisconsin/SSEC/CIMMS, 6ESSIC/UMCP, 7ADNET
Cloud Mask, Cloud Top, Optical/Microphysical Properties: S. Platnick1, K. Meyer1, G. Wind2,1, N. Amarasinghe2,1, C. Wang3,1, C. Peterson4, E. Borbas5, R. Holz5, P. Veglio5, et al.
Aerosol DT: R. Levy1, V. Sawyer2,1, S. Mattoo2,1, et al.
Clear Sky: E. Borbas5
Aerosol DB: C. Hsu1, V. Kim6, J. Lee6, et al.
Atmosphere Team Level-3: P. Hubanks7,1, S. Platnick1, K. Meyer1

## Slide 2
Atmo. C7, MODIS/VIIRS STM, May. 2023
    New algorithm based on A-SIPS Yori software package to improve flexibility/maintenance.
    Provides scalar/multi-dimensional statistics consistent with current MOD/MYD08
        Change from C6.1: separate L3 daily and monthly product files for each L2 Atmosphere science product (e.g., cloud, aerosol, etc.). Discontinue 8-day aggregation?
    NetCDF-4 with same internal variable formatting as CLDPROP_L3
    Initial work started in spring 2020. In testing in MODAPS for C7 cloud products, recently were able to scale up for more efficient processing. Code for aerosol and clear sky products in development.
C7 Atmosphere Team L3: MOD/MYD08
See Paul Hubanks et al. poster
Notes: Yori: Python

## Slide 3
Atmo. C7, MODIS/VIIRS STM, May. 2023
Major algorithm updates
    Approach: Leverage common science modules with CLDMSK/CLDPROP v2 products to improve maintainability, science.
    New algorithms (ROSES 2017) with some science testing started in MODAPS
            IR Optimal Estimation (IROE) for 1km cloud-top height and ice cloud optical thickness/particle effective size retrievals [Wang et al., 2016a,b], old version. Parallel/updated testing at A-SIPS.
            Pixel-level radiative fluxes (RRTMG code). Parallel testing at A-SIPS.
            1.38µm cirrus cloud optical thickness retrievals [Meyer & Platnick, 2010]
    New algorithm to be integrated by MODAPS
        Random Forest cloud phase [Wang et al., 2020]. Latest version of code sent to SDST (STIG) a couple of months ago. Parallel testing at A-SIPS for eventual integration into CLDPROP.
    Experimental efforts to be evaluated
            Improved retrieval failure metric (RFM): extended liquid CER valid range (4-50µm)
            High-resolution 500m optical property retrievals
    Cloud forward radiative model: updated liquid refractive index datasets for consistency with CLDPROP [Platnick et al., 2020] currently under testing.
C7 Clouds: MOD/MYD06 Optical and 1km Cloud Top

## Slide 4
Atmo. C7, MODIS/VIIRS STM, May. 2023
New pixel-level SW and LW broadband radiative flux calculations (TOA, sfc) using cloud property retrievals as input and GEOS-IT (incl. aerosol information needed to characterize optical properties for clear sky calculations).
Cloud-top 1km properties algorithm (IROE) that also provides day/night ice cloud optical properties and enables leveraging AIRS and CrIS sounder absorption channels.
See Colten Peterson et al.
surface flux evaluation poster
See Chenxi Wang et al. poster
C7 Clouds: MOD/MYD06 Optical and 1km Cloud Top
Notes: Advertisement

## Slide 5
Atmo. C7, MODIS/VIIRS STM, May. 2023
Other algorithm updates
          Transition to GEOS-IT atmospheric profile and snow cover ancillary dataset. Available for testing.
          NetCDF-4 file format (all Atmosphere products)
          Improved pixel-level uncertainties
          Updated atmospheric corrections
          Various QA updates under consideration:
                Clear sky restoral and multilayer flag algorithm updates
                Improved metadata descriptions and status flags
C7 Clouds: MOD/MYD06 Optical and 1km Cloud Top

## Slide 6
Atmo. C7, MODIS/VIIRS STM, May. 2023
          Transition to GEOS-IT atmospheric profile and snow cover ancillary dataset
            Eliminate the need for NSIDC NISE and NOAA Optimum Interpolation SST.
            Reduce blockiness due to the low spatial resolution of ancillary data (atmospheric profiles)
          QA updates:
                Lower confidence level for high (> 900 hPa) CTP (CTH) values when Cloud Mask indicates cloudy or probably cloudy.
C7 Clouds: MOD/MYD06 5km Cloud Top
C7 Clouds: MOD/MYD35 Cloud Mask
          MOD35 will be replaced with continuity algorithm (MVCM), including updated reflectance tests.
          Transition to GEOS-IT atmospheric profile and snow cover ancillary dataset
          Update of night ocean and snow fraction thresholds for GEOS-IT
          Updates related to Terra Printed Wire Assembly (PWA) failures

## Slide 7
Atmo. C7, MODIS/VIIRS STM, May. 2023
C7 Aerosol Deep Blue (DB): MOD/MYD04
          C7 algorithm based on VIIRS DB v2 algorithm for consistency between sensors
          C7 algorithm will no longer be dependent on PGE toolkits. (Same for Dark Target)
          MOD/MYD04 L2 will have different SDS structure compared to C6.1
          Initial draft of the C7 DB science codes will be ready before the end of 2023
            A long-term record of C7 L1b data is necessary for algorithm development and any potential additional calibration adjustment. (Same for Dark Target)

## Slide 8
Atmo. C7, MODIS/VIIRS STM, May. 2023
C7 Aerosol Dark Target (DT): MOD/MYD04
          MODIS C7 algorithm is based on team’s MEaSUREs “DT-Package” that allows for consistency between sensors.
            MODAPS has shown they can run the DT-Package code, with outputs
          10 km product: will have different SDS structure (separate geolocation and geophysical) compared to C6.1, although DT variable names will be identical. Note: case conventions are consistent with VIIRS (e.g., “Solar_Zenith” versus “solar_zenith”).
            Discussing with DB whether to keep the same (e.g., NDVI-based) merge of DT/DB in the MOD04_L2 product or make updates.
          3 km product (MxD04_3K): also use the DT-Package, with major update that scan lines will be re-ordered monotonically by latitude to mitigates bow-tie.
          Anticipate a few science updates that have been tested, but not implemented in the current algorithm. Recently concentrating on MEaSUREs (GEO) and VIIRS (v2) processing but need to circle back to C7 science.

## Slide 9
Atmo. C7, MODIS/VIIRS STM, May. 2023
C7 Clear Sky: MOD/MYD07 and 05
MOD/MYD07 – Atmosphere Profiles
          Transition to GEOS-IT form GDAS
          Update SRF shifts and detector config files after the C7 L1B data processing*
          Update regcoefs (format from bin to NetCDF4) after the C7 L1B data processing*
          Update training data with the latest Emissivity Atlas (CAMEL V3)
          Small bug fixes with units, top layers of moisture profile, the inversion over ice etc.
          QA updates for inversions over ice, Terra/TOZ (due to the B30 issue)
MOD/MYDDS – Destriping Algorithm
          Update configuration files after the C7 L1B data processing*
MOD/MYD85 – Clear Sky Bias Algorithm
          Transition to GEOS-IT.
*involves the delivery of two text/NetCDF4 files

## Slide 10
Atmo. C7, MODIS/VIIRS STM, May. 2023
    C7 (cloud team) science testing turnaround has slowed over past couple of years. Do we have sufficient SDST personnel to engage both the Atmosphere and Land algorithm teams? If not, how are priorities determined?
    Capability of MODAPS to support C7 reprocessing once C7 L2+ code is finalized?
    C7 L1B testing/evaluation in process.
    With SDST help, successfully created alternative to OISST (for C6.1 forward processing, C7 will use GEOS-IT); NSIDC NISE likely to be continued through MODIS lifetime!
    Change to Ubuntu and GitLab over last couple of years has been a challenge.
      Code delivery/testing in GitLab environment, creation of unit tests, remains problematic.
      Was the move to GitLab worth the effort (e.g., improve algorithm delivery productivity/tracking) given that this is the last major Collection update for Atmospheres?
    Specific team tech. issues:
        Usability of Windhoek (team machine), CEPH buckets (open-source storage solution), etc.
        U. Wisconsin: Local machine no longer viable to support PGEs. User account on MODAPS or Windhoek would be very beneficial to help solve technical issues with being outside the firewall. Request from Nov. 2021.
C7 Atmosphere Team – Looking Forward