## Slide 1: VIIRS Nighttime Lights Algorithm Development 2015
Chris Elvidge
Earth Observation Group (EOG)
NOAA National Centers for Environmental Information
(formerly NGDC)
Kimberly Baugh, Feng Chi Hsu, Mikhail Zhizhin, Tilottama Ghosh
Cooperative Institute for Research in Environmental Science
University of Colorado
Emails: kim.baugh@noaa.gov, chris.elvidge@noaa.gov

## Slide 2
Nighttime Lights Composites
(Historical OLS Products)
The EOG Group at NCEI has a long history of making global annual nighttime lights composite products using DMSP-OLS data.
http://www.ngdc.noaa.gov/eog/dmsp/downloadV4composites.html

## Slide 3
Nighttime Lights Composites
What are they?
A nighttime lights composite is made to serve as a baseline of persistent light sources.
Composites are made as an average of the highest quality nighttime lights imagery over desired time period – usually monthly or annually.
“Stable Lights” composites have ephemeral light sources and non-light (background) areas are removed from a composite.
EOG group is producing current monthly cloud-free/no-moon DNB nighttime lights composites and is doing algorithm development to turn these in to Stable Lights composites.

## Slide 4
Nighttime Lights Composites
What goes in?
Only the “highest quality” nighttime data gets averaged into a composite
Currently this is defined as DNB data that is:
  Cloud-free (using the VIIRS cloud-mask (VCM) product)
  Nighttime with solar zenith angles greater than 101
  Not affected by moonlight (lunar illuminance < 0.0005 lux)
  Middle of swath (DNB has increased noise at edge of scan)
  Free of lights from lightning
  Free of “lights” from South Atlantic Anomaly

## Slide 5
Nighttime Lights Composites
(Monthly DNB Products)
http://www.ngdc.noaa.gov/eog/viirs/download_monthly.html
Monthly DNB nighttime lights composites are available online
Globe is cut into 6 tiles to reduce individual file sizes
These products still contain ephemeral lights and non-lights (background).

## Slide 6
Sources of Nighttime Lights
Cities and human settlements
Industrial Sites
Boats
Gas Flares
Aurora
Fires
Lightning

## Slide 7
Stable Sources of Nighttime Lights
Cities and human settlements
Industrial Sites
Boats
Gas Flares
Aurora
Fires
Lightning

## Slide 8
DNB Image Artifacts
In addition to ephemeral lights, there are sensor specific image artifacts that need to be removed.
The four most troublesome artifacts:
  Stray Light
  High energy particle hits to detector – most common in South Atlantic Anomaly (SAA) region
  Cross talk – across lines within a scan when imaging very large gas flares
  DNB aggregation zones 29-32

## Slide 9: DNB Image Artifacts: Stray Light
Northrup Grumman algorithm was implemented at the IDPS in August 2013.
Does a good job of mitigating stray light effects for visual interpretation.
Some issues for algorithm development within the stray light corrected region:
  Can under/over-correct, especially at transition into stray light and in Southern hemisphere
  Variance of data across scan is altered
  Correction quality is dependent on time from correction lookup table generation
Stray light corrected regions are identified and processed separately

## Slide 10: DNB Image Artifacts: SAA Hits
Example of high values in DNB due to high energy particles in South Atlantic Anomaly region.
Red pixels were labelled as SAA hits because they exceeded the average of neighboring pixels by more than 99.5%
This algorithm removes most of the SAA noise
In prototype composites, there appears to be remaining SAA noise with low radiance values. Further investigation is warranted.
March 31, 2012 – off coast of Brazil

## Slide 11: DNB Image Artifacts: Crosstalk
Crosstalk is only an issue in High Gain State (HGS) DNB data
Crosstalk manifests as spurious signal in the same sample position in other detectors within the scan.
Crosstalk is seen mainly (only?) over large gas flares
Both positive and negative crosstalk occurs
Algorithm for detection of crosstalk events is TBD
Crosstalk shows up as pairs of small “lights” around large gas flares in Persian Gulf DNB composite.
May 2014 average DNB composite

## Slide 12: DNB Image Artifacts: Agg. Zones 29-32
DNB
Aggregate SVDNB_npp_d20121018_t0749150_e0754554_b05050_c20121018135455638495_noaa_ops.h5
Increased noise
at edge of scan
Edge-of-swath pixels are discarded due to increased noise
(DNB aggregation zones 29-32).

## Slide 13: DNB Ephemeral Lights: Lightning
A
B
Lightning
Detected
Lightning
A
B
Rise at scan boundary exceeds threshold for N consecutive along-scan pixels
Lightning appears in DNB imagery as horizontal ribbons of lighting.
These features are generally one scan (16 lines) wide.
When lightning features are in adjacent scans, they are generally offset and the brightness values differ, so algorithm still holds.

## Slide 14
First approach:
  Separate fires from lights using VIIRS NightFire (VNF) product
  VNF algorithm uses VIIRS M-band data, collected simultaneously with DNB
DNB Ephemeral Lights: Fires/Flares/Volcanos
Issues:
1) Remaining glow around VNF detections need to be addressed.
2) DNB has lower detection limits than the M-bands and picked up some fires that VNF did not detect.
Some fires not detected by VNF

## Slide 15
Second approach:
  Create histograms of DNB radiances using an extended time series (annual)
  Use histograms to identify and remove outliers
  Similar to algorithm developed for DMSP-OLS Stable Lights
  Advantages: This algorithm removes ANY outliers, including fires, boats, unfiltered-SAA, crosstalk, …
  Disadvantages: Persistent flares and volcanic activity can remain. Method requires long time-series of data.
DNB Ephemeral Lights

## Slide 16
DNB Ephemeral Lights: Outlier Removal
Odisha, India 2014 DNB Composite
Histograms are made for each grid cell in composite
DNB radiance values are placed in discrete bins based on log transform. Bin=floor(100*(log(1E9*Rad+1.5))
Example histogram of small village

## Slide 17
DNB Ephemeral Lights: Outlier Removal
Example histograms of grid cells containing fires

## Slide 18
DNB Ephemeral Lights: Outlier Removal
Algorithm:
Compute standard deviation of observations
Remove highest observation
Re-compute standard devation
Repeat steps 2-3 if difference in standard deviations > threshold
Re-compute average of remaining observations
Outlier removal algorithm removed top 4 observations:

## Slide 19
DNB Ephemeral Lights: Before Outlier Removal
Toggle with next slide
Notice how regions with fire activity return to background radiance levels after outlier removal

## Slide 20
DNB Ephemeral Lights: Before Outlier Removal
Toggle with previous slide
Notice how regions with fire activity return to background radiance levels after outlier removal

## Slide 21: DNB Background Removal
  The DNB’s detection limits are low enough, that even without moonlight present, nocturnal airglow can light up terrain and high albedo surfaces, making it challenging to separate dim lights from high albedo surfaces.
2014 DNB Composite over Southern Pakistan – some road features have lower average radiance values than no-light areas with high albedo
2014 DNB Composite over Himalayas – snow-covered peaks have higher average radiances than some of the villages

## Slide 22: DNB Background Removal
Current approach:
  Create 5X5 pixel histograms of DNB radiances after outlier removal using an extended time series (annual)
  Analyze histograms for existence of a “pure background” grid cell using mean and standard deviation.
  For each composite grid cell, get “closest” pure background grid cell. Remove its background and re-average to get lights-only average.
Foreseen challenges
  Known discontinuities in offsets of DNB calibration (monthly?)
  SRF changes in DNB over time could affect this work
  Defining “closest” in terms of which background grid cell to use

## Slide 23: Nighttime Lights Composites: Next Steps
  Finalize background characterization/removal algorithm
  Test outlier removal algorithm on aurora
  Add in Nightfire detections to identify locations of persistent flares and volcanos
  Apply atmospheric correction algorithm to DNB radiances

## Slide 24: Questions?
  Emails:
  Kim.Baugh@noaa.gov
  Chris.Elvidge@noaa.gov

## Slide 25: Backup Slides

## Slide 26: VIIRS Nighttime Lights Composite – 2015/01 Excluding Stray Light Corrected Areas

## Slide 27: VIIRS Nighttime Lights Composite – 2015/01 Including Stray Light Corrected Areas