## Slide 1
Remote Sensing Reflectance
and Derived Ocean Color Products from MODIS to VIIRS
MODIS Science Team Meeting
19-22 May 2015, Silver Spring, MD
Bryan Franz
Ocean Ecology Laboratory
NASA Goddard Space Flight Center

## Slide 2: Proposal Team: MODIS & VIIRS
Team Member | Primary Role
Bryan Franz | project lead & quality assessment
Zia Ahmad | atmospheric correction
Sean Bailey | vicarious calibration & software
Gene Eplee | VIIRS calibration
Gerhard Meister | MODIS calibration
Chris Proctor | in situ validation
Kevin Turpie | VIIRS prelaunch
Jeremy Werdell | bio-optical algorithms
and the Ocean Biology Processing Group ...
Notes: draw on expertise of entire team for software development, processing, analysis, and documentation

## Slide 3: 2014.0 Multi-Mission Ocean Reprocessing
Scope
OC from CZCS, OCTS, SeaWiFS, MERIS, MODIS(A/T), and VIIRS
SST from MODIS
Motivation
improve interoperability and sustainability of the product suite by adopting modern data formats, standards, and conventions
incorporate algorithm updates and advances from community and last MODIS Science Team developed since 2010 (last algorithm change)
incorporate knowledge gained in instrument-specific radiometric calibration and updates to vicarious calibration
Status
OC from OCTS & VIIRS done, MODISA in progress
SST from MODISA and MODIST done (not yet released)
Notes: tied to MODIS science team, new algorithm development
7 instruments

## Slide 4: Remote Sensing Reflectance (Rrs; sr-1)
Rrs is the ratio of upwelling “water-leaving” radiance to downwelling irradiance, just above the sea surface
Rrs is the fundamental remote sensing quantity from which most ocean color products are derived (e.g., chlorophyll, particulate organic and inorganic carbon, inherent optical properties)
Rayleigh
aerosol + Ray-aer
foam & whitecaps
Sun glint
water-leaving
observed TOA
Atmospheric Correction

## Slide 5: adaptation to VIIRS
algorithm modifications limited to adjustment for sensor-specific spectral band centers and relative spectral responses
same Ahmad-Fraser vector radiative transfer code used to derive MODIS & VIIRS-specific Rayleigh and aerosol model tables
bands used for aerosol determination
  MODIS: 748 & 869 nm
  VIIRS: 745 & 862 nm

## Slide 6: Rrs(l) for Spring 2012
VIIRS 443 nm
VIIRS 551 nm
MODISA 443 nm
MODISA 547 nm

## Slide 7: Chla for Spring and Fall 2012
VIIRS Spring
VIIRS Fall
MODISA Spring
MODISA Fall

## Slide 8: Global Mid-Latitude (+/- 40°) Chlorophyll Anomaly showing suspect trend in VIIRS R2013.1
Following Franz, B.A., D.A. Siegel, M.J. Behrenfeld, P.J. Werdell (2014). Global ocean phytoplankton [in State of the Climate in 2013]. Bulletin of the American Meteorological Society, 95(7), S78-S80.
SeaWiFS
MODISA
NASA VIIRS
MERIS
Multivariate Enso Index (MEI)
VIIRS
trend issue
VIIRS
trend issue
before latest reprocessing

## Slide 9: VIIRS R2014.0 calibration
Significantly improved instrument calibration developed for ocean color through re-analysis of VIIRS prelaunch and on-orbit calibration.
Based on solar calibration, corrected with lunar calibration.
Incorporating advancements in solar and lunar calibrator knowledge (solar diffuser stability, solar unit vector fix, lunar libration corrections, etc.).
implemented as a continuous calibration model that allows for extrapolation into the future (improved NRT calibration quality).
Including corrections for relative detector and mirror-side calibration to reduce image striping artifacts.
Robert E. Eplee, Kevin R. Turpie, Gerhard Meister, Frederick S. Patt, Bryan A. Franz, and Sean W. Bailey, "On-orbit calibration of the Suomi National Polar-Orbiting Partnership Visible Infrared Imaging Radiometer Suite for ocean color applications," Appl. Opt. 54, 1984-2006 (2015)
Notes: lunar-based
exponential model allows forward-stream extrapolation
relatively accurate NRT retrievals
destriping

## Slide 10: VIIRS Reduced Image Striping
Revised instrument calibration includes detector relative calibration to reduce image striping artifacts.
Version R2013.1
Version R2014.0
Notes: improved front detection

## Slide 11: VIIRS Clear-Water Rrs(l) Time-Series Comparison Before & After R2014.0 Reprocessing
412
443
486
551
before
after

## Slide 12: VIIRS Clear-Water Rrs Anomaly Trends
Chlorophyll
Rrs(443)
Rrs(551)
Before Reprocessing
R2013.1

## Slide 13: VIIRS Clear-Water Rrs Anomaly Trends
Chlorophyll
Rrs(443)
Rrs(551)
After Reprocessing
R2014.0

## Slide 14: Global Mid-Latitude (+/- 40°) Chlorophyll Anomaly showing improved agreement of VIIRS with MODISA, MEI, and historical norms after R2014.0 reprocessing
VIIRS R2013.1
VIIRS R2014.0
Following Franz, B.A., D.A. Siegel, M.J. Behrenfeld, P.J. Werdell (2015). Global ocean phytoplankton [in State of the Climate in 2014]. Bulletin of the American Meteorological Society, submitted.
SeaWiFS
MODISA
NASA VIIRS
MERIS
SeaWiFS
MODISA
NASA VIIRS
MERIS
Multivariate Enso Index (MEI)
Multivariate Enso Index (MEI)
calibration issue
resolved
VIIRS R2013.1
VIIRS R2014.0

## Slide 15: MODISA Calibration Issues
Collection 6 calibration and subsequent updates are being applied, but standard calibration may not be sufficient to fully characterize late-mission temporal calibration changes to level required for ocean color.
MODIS/Aqua Rrs showing increased temporal variability in blue (412, 443) water-leaving reflectance trends after 2011. Is it real?

## Slide 16: MODISA Rrs(l) Deep-Water Time-Series
increasing variability
412
443
Processing Version R2013.1

## Slide 17: MODIS Calibration Issues
Collection 6 calibration and subsequent updates are being applied, but standard calibration may not be sufficient to fully characterize late-mission temporal calibration changes to level required for ocean color.
MODIS/Aqua Rrs showing increased temporal variability in blue (412, 443) water-leaving reflectance trends after 2011. Is it real?
In 2014, all radiometry shifted (up in blue, down in green), with commensurate decline of 10% in clear-water chlorophyll.

## Slide 18: MODISA Clear-Water Rrs Anomaly Trends
2014 anomaly
“calibration issue”
Chlorophyll
Rrs(443)
Rrs(547)
Current Operational
R2013.1

## Slide 19: MODIS Calibration Issues
Collection 6 calibration and subsequent updates are being applied, but standard calibration may not be sufficient to fully characterize late-mission temporal calibration changes to level required for ocean color.
MODIS/Aqua Rrs showing increased temporal variability in blue (412, 443) water-leaving reflectance trends after 2011. Is it real?
In 2014, all radiometry shifted (up in blue, down in green), with commensurate decline of 10% in clear-water chlorophyll.
Our team and MCST have been working to resolve these issues in preparation for MODISA reprocessing 2014.0, with some success.

## Slide 20: MODISA Clear-Water Rrs Anomaly Trends
Chlorophyll
Rrs(443)
Rrs(547)
Reprocessing Test Results
MCST LUT V6.1.33.8_OC2
+ OBPG cross-scan corrections
2014 anomaly
“resolved”
Notes: more variability in early mission

## Slide 21: MODISA & VIIRS Rrs(l) Clear-Water Time-Series showing “good” agreement
412
443
MODISA Processing Test Results
486-488
547-551

## Slide 22: MODISA & VIIRS Rrs(l) Deep-Water Time-Series showing “good” agreement
412
443
MODISA Processing Test Results
486-488
547-551
MODIS
VIIRS
Ratio

## Slide 23: VIIRS R2014.0 In Situ Validation
Rrs(443)
Rrs(547)
Chla

## Slide 24: MODISA R2013.1 In Situ Validation
Rrs(443)
Rrs(547)
Chla

## Slide 25: MODISA showing agreement with R2014.0 VIIRS Chlorophyll (OCI) Deep-Water Time-Series
MODISA & VIIRS R2014.0 Test Results
4-day means (not monthly)
VIIRS
MODISA
 | Mean | Stdv | 
MODISA | 0.069 | 0.009 | mg m-3
VIIRS | 0.068 | 0.008 | mg m-3
VIIRS/MODISA | 0.99 | 0.04 | 

## Slide 26: Summary
MODIS continuity algorithm for the retrieval of Rrs and Chlorophyll (and other derived products) has been implemented for VIIRS.
VIIRS Rrs temporal stability is much improved following extensive recalibration effort, and range of variability is now consistent with historical norms following VIIRS Reprocessing 2014.0.
MODIS-Aqua temporal variability has increased in the blue since 2011, with a large departure in all bands in 2014. Efforts have been made to address these issues with some success.
MODIS-Aqua and VIIRS Rrs and derived Chlorophyll are comparable in magnitude and spatial distribution, show a similar level of agreement with in situ validation, and show good temporal consistency (based on latest test results).
MODISA Reprocessing 2014.0 in progress!

## Slide 27: Summary
MODIS-Terra calibration updates and reprocessing will be addressed once MODIS-Aqua reprocessing is complete.

## Slide 28: back-up

## Slide 29: determining aerosol contribution
assume Lw(l) = 0 at two NIR (or SWIR) bands, or that it can be estimated with sufficient accuracy.
retrieve aerosol reflectance in each NIR band as
use spectral dependence of retrieved NIR aerosol reflectance (e) to select the most appropriate aerosol model from a suite of pre-computed models
use NIR aerosol reflectance and selected aerosol model to extrapolate aerosol reflectance to visible wavelengths
known

## Slide 30: aerosol model tables
vector RT code (Ahmad-Fraser)
based on AERONET size distributions & albedos
80 models (10 size fractions within 8 humidities)
  100% coarse mode to 95% fine mode
  non- or weakly absorbing
LUT: extinction, albedo, phase function, ss->ms, td
  function of path geometry (or scattering angle)
model selection discriminated by relative humidity
Typical Size Distributions
Ahmad et al. 2010, Appl. Opt.
Rh rvf σf rvc σc rvf/rovf rvc/rovc
0.30 0.150 0.437 2.441 0.672 1.006 1.009
0.50 0.152 0.437 2.477 0.672 1.019 1.024
0.70 0.158 0.437 2.927 0.672 1.063 1.210
0.75 0.167 0.437 3.481 0.672 1.118 1.439
0.80 0.187 0.437 3.966 0.672 1.255 1.639
0.85 0.204 0.437 4.243 0.672 1.371 1.753
0.90 0.221 0.437 4.638 0.672 1.486 1.917
0.95 0.246 0.437 5.549 0.672 1.648 2.293
Mean AERONET Fine & Coarse Modal Radii
Fine Mode Albedo

## Slide 31: aerosol model selection & application
model epsilon
select the two sets of 10 models (10 size fractions) with relative humidity (RH) that
bound the RH of the observation.
find the two models that bound the observed epsilon within each RH model family.
use model epsilon to extrapolate to visible.
compute weighted average, , between
models within each RH family, and then again between bounding RH solutions.
*actually done in single scattering space and transformed to multi-scattering
*

## Slide 32: we estimate Lw(NIR) using a bio-optical model
  1) convert Lw(670) to bb/(a+bb)
  via Morel f/Q and retrieved Chla
  2) estimate a(670) = aw(670) + apg(670)
  via NOMAD empirical relationship
  3) estimate bbp(NIR) = bbp(670) (l/670)h
  via Lee et al. 2002
  4) assume a(NIR) = aw(NIR)
  5) estimate Lw(NIR) from bb/(a+bb)
  via Morel f/Q and retrieved Chla
guess
Lw(670) = 0
model
Lw(NIR) = func Lw(670)
correct
L'a(NIR) = La(NIR) – t Lw(NIR)
retrieve
Liw(670)
test
|Lwi+1 (670) - Liw(670)|
< 2%
no
done
Bailey et al., Optics Express, 2010

## Slide 33: brdf correction
Rrs() = R’rs() fb(,θ0,θ,Dj,Chl,w)
Chl = f (Rrs(l))
iteration
to account for shape of sub-surface light-field due to position of the
Sun and optical properties of the water column.
based on pre-computed look-up tables from hydrolight simulations of
Morel et al. 2002, Appl. Opt.
given radiant path geometry (θ0,θ,Dj), windspeed (w) and Chl
Chl = f (R’rs(l))
fb(,θ0,θ,Dj,Chl,w) = (R0 f0/Q0) / (R f/Q)
f/Q relates subsurface irradiance reflectance to radiance reflectance
R includes all reflection/refraction effects of the air-sea interface
θ0=0, θ=0,Dj=0
Notes: may not want to apply brdf for IOP retrieval

## Slide 34: adaptation to VIIRS
standard MODIS atmospheric correction software was modified (previous S-NPP science team) to also process VIIRS
starts from VIIRS pseudo Level-1A (SDR with no temporal calibration), and applies instrument calibration in Level-1A to Level-2
  pseudo Level-1A to be replaced by NASA Level-1A (when operational)
  instrument calibration developed by OBPG (Eplee et al. 2015)
algorithm modifications limited to adjustment for sensor-specific spectral band centers and relative spectral responses
same Ahmad-Fraser vector radiative transfer code used to derive MODIS & VIIRS-specific Rayleigh and aerosol model tables
bands used for aerosol determination
  MODIS: 748 & 869 nm
  VIIRS: 745 & 862 nm