## Slide 1
Developing a Long-term Global Reservoir Product Series by Fusing Multi-Satellite Observations
November 11/18-21, 2019
MODIS/VIIRS Science Team Meeting
Huilin Gao, Gang Zhao, Yao Li
Department of Civil&Environmenatl Engineering
Texas A&M University

## Slide 2
Global Reservoir and Dam (GRanD) Database
Lehner et al., 2011
Global capacity > 6200 km3
Chao et al., 2008
Global Reservoirs

## Slide 3
Reservoir Storage vs. Reservoir Evaporation
Hydropower
Irrigation/water supply
Flood control
Recreation
Evaporation > Industrial + Domestic
~265 km3 in 2010
https://www.flickr.com/photos/89241789@N00/172762894
Lake Mead annual evaporation =791,000 acre-feet

## Slide 4
Motivation
FUTURE NEEDS.
Uniform, coherent, and long-term measurements.
Friedrich et al., 2017 BAMS

## Slide 5
Objectives
To generate a comprehensive, coherent, and long term global reservoir product series at improved spatial coverage (and at improved temporal resolution) by combining MODIS/VIIRS observations with data from other satellite sensors.
Develop a long term reservoir storage variation dataset under all-weather conditions.
Generate a first long term record of the reservoir evaporation rate and the evaporation loss.
Validate the reservoir product series and quantify the uncertainties associated with the datasets.

## Slide 6
Storage variations
Elevation
Altimetry
(Radar/Lidar)
Area
MODIS/VIIRS
A-E relationship
Reservoir Storage Variations
5
Vo = Vc – (Ac+Ao)(hc-ho)/2
Satellite combination | A-E relationship | Sample number | R2
Radar-MODIS (RM) | y = 0.146x + 285.18 | 118 | 0.92
Radar-Landsat (RL) | y = 0.158x + 280.57 | 58 | 0.96
ICESat-MODIS (IM) | y = 0.152x + 281.33 | 14 | 0.91
ICESat-Landsat (IL) | y = 0.199x + 263.15 | 10 | 0.99
A-E relationship at Lake Mead

## Slide 7
Spatial Coverage of the Dataset
347 reservoirs (3123 km3 , 50% of global capacity)
60 km
Radar altimeter track
4 km
ICESat altimeter track

## Slide 8
Algorithm for Bathymetry (A-E relationship)
Data
Landsat-based water classfications
Surface Water Occurrence (SWO) from Global Surface Water (GSW) dataset (Pekel et al., 2016)
Global Reservoir Surface Area Dataset (GRSAD) (Zhao and Gao, 2018)
Stallite altimetry dataset
ICESat/GLAS lidar altimetry dataset
Global Reservoir and Lake Monitor (G-REALM)
Hydroweb
(Li et al., 2019)
(Gao et al., 2012)

## Slide 9
Derive A-E relationships
Bathymetry Results

## Slide 10
Bathymetry Results

## Slide 11
Validations of A-E & E-V Relationships
A-E relationships
E-V relationships
Li et al, RSE, in review.

## Slide 12
Lake area based on MODIS classification

## Slide 13
Validation of the MODIS-based Storage

## Slide 14
Evaporation loss
Evaporation rate
MODIS LST, area
+ meteorology data
Reservoir Evaporation Estimation
Area X evaporation rate
Storage variations
Elevation
Altimetry
(Radar/Lidar)
Area
MODIS/VIIRS
Area-elevation curve
Vo = Vc – (Ac+Ao)(hc-ho)/2

## Slide 15
Heat storage effect:
Spring and Summer – absorb heat
Fall and Winter – release heat
Air Temperature (ºF)
Evaporation (inch)
Jul
Sep
Lake Tahoe 2014
Penman Equation
: slope of the saturation vapor pressure curve (kPa·ºC-1)
: net radiation (MJ·m-2·d-1)
: psychrometric constant (kPa·ºC-1)
: wind function (s·m-1)
: vapor pressure deficit (kPa)
: latent heat of vaporization (MJ·kg-1)
Heat Storage Effect on the Evaporation Rate
Wind function

## Slide 16
Improving the Estimation of Reservoir Evaporation Rate
Lake Tahoe
(Friedrich et al., 2017)
15
(L)
Dynamic
MODIS Area
(McJannet et al. 2012)
Zhao and Gao, RSE, 2019.

## Slide 17
Improving the Estimation of Reservoir Evaporation Rate
Translate MODIS LST to
temperature profile &
Calculate evaporation rate
Lake Temperature Evaporation Model (LTEM)
16

## Slide 18
Evaporation Validation Locations
17

## Slide 19
Temperature Profile Validation Results
Good agreement for mixing depth and temperature seasonality
Overall, long-term biases range from -0.5 °C to 0.5 °C
Monthly value biases range from -5.4 °C to 6.0 °C
Oneida Lake
Lake Mead
Lake Biwa
Lake Mendota
Lake Ammersee
18

## Slide 20
Evaporation Rate Validation Results
Average R2 increase: 0.28
More improvement for deep lakes (e.g. Mead: 0.44)

## Slide 21
Evaporation Results for Lake Nasser
Zhao and Gao, Estimating lake temperature profile and evaporation losses by leveraging MODIS LST data (in prep)

## Slide 22
Summary
By leveraging MODIS observations along with satellite altimetry data, the spatial and temporal coverage of remotely sensed global reservoirs can be significantly improved.
High quality A-E relationship can be achieved using Landsat and altimetry data.
By using MODIS LST to calculate the heat storage and considering fetch as a function of the dynamic lake area, reservoir evaporation rate can be better .
Both the storage and evaporation algorithms have been validated using in situ data.
Future work will focus on applying the algorithms to generate reservoir storage and evaporation product using both MODIS and VIIRS.
Li et al., A high-resolution bathymetry dataset for global reservoirs using multi-source satellite imagery and altimetry, Remote Sensing of Environment, in review.
Zhao and Gao, Estimating reservoir evaporation losses for the United States: Fusing remote sensing and modeling approaches, Remote Sensing of Environment, 226, 109-124, 2019.