## Slide 1
An Update on the
Airborne Lunar Spectral Irradiance
(Air-LUSI)
K. Turpie, UMBC / JCET
MODIS/VIIRS Calibration Workshop
26 February 2021

## Slide 2
Air-LUSI
AITT Program Team
Kevin Turpie, PI (UMBC/GSFC 616.2)
Steve Brown, Co-I (NIST)
John Woodward, Co-I (NIST)
Andrew Gadsden, Co-I (U of Guelph)
Tom Stone, Co-I (USGS)
Andrew Newton (U of Guelph)
Steve Grantham (NIST)
Tom Larason (NIST)
Stephen Maxwell (NIST)
Joe Rice (NIST)

## Slide 3
3
ADVANCEMENT OF ABSOLUTE LUNAR CALIBRATION
Lunar calibration potentially can provide cost-effective absolute calibration of reflected solar bands that is accurate and inter-consistent across multiple sensors.
Benefits
A permanent (and retrospective) common reference not affected by climate.
Inter-consistent Earth climate data records across series of missions and data gaps.
Intercalibration of sensors between international partners.
Enable future constellation architectures and very small or inexpensive platforms.
Enhanced calibration for aquatic remote sensing.
Cost: Low
Steps
Improve lunar calibration reference:
  - Acquire high-accuracy, SI-traceable measurements of the Moon.
  - Use new measurements to advance the lunar model.
Improve techniques for lunar measurements by satellite sensors.

## Slide 4
Air-LUSI
Objectives
4

## Slide 5
NASA ER-2
Altitude
69,000 ft
21 km
Superpod
Mid-body
Aft-body
Fore-body
The telescope and robotic mount are in Superpod Aft-body.
The sensor enclosure and control computer are in Mid-body.
IRIS telescope views to port through Aft-body Zenith Viewport.
Aft-body
Zenith
Viewport
ABOVE
RIGHT
BELOW
RIGHT
5
Air-LUSI
ER-2 Aircraft

## Slide 6
ARTEMIS – Autonomous, Robotic TElescope Mount Instrument Subsystem
    Uses tracking camera on telescope and computer controlled PID loop.
    Keeps telescope fixed on the Moon to within 0.1°.
IRIS – IRradiance Instrument Subsystem
    A non-imaging telescope (integrating sphere at focal point).
    Light fed via a fiber optic cable to a spectrograph.
    On-board LED validation source.
    Instrument enclosure keeps the spectrograph and validation source at surface-level P & T during flight.
ARTEMIS Control Assembly
ARTEMIS Control Assembly
Installation
ARTEMIS Mount
IRIS Telescope
ARTEMIS
Tracking Camera
IRIS
Instrument Enclosure
IRIS Fiber Optics
Cable Harness
IRIS Instrument Enclosure
Installation
Pilot Switch Simulator
Instrument Subsystems
IRIS Telescope in view port
6
Notes: What is your critical path? A bulleted list of steps to our objective. Get h/w ready for engineering test for lunar obs late in May.

## Slide 7
Robotic Telescope system employs a tracking camera and image recognition software to keep the telescope boresight continuously aligned with the Moon in flight to within 0.1°.
Air-LUSI
Robotic Telescope

## Slide 8
8

## Slide 9
9

## Slide 10
Robotics
Air-LUSI network
and telemetry
Instrument
Function
Mobile Pilot
Communication
Air-LUSI “Mission Control”
10

## Slide 11
11
Notes: This is the chase car. Yes, those are fins on the back. They're to let everyone know that this car can really fly down runaway. Having been in the vehicle, they seem superfluous.
The mobile pilot (another ER-2 pilot) follows with plane in the car as it taxis to the runway. Once there, he circles the plane before take off for a final check. Then, we chase the plane down the runway during takeoff. It's a short ride.

## Slide 12
12
Notes: The ER-2 can climb very rapidly. It reaches 40K ft in about 10 mins.
I text to the team back in the control room in the hangar, now about a 1 mile away, that the plane has left the ground. The response: We know.
The engine on the plane is very powerful, and very noisy. Ear protection is entirely necessary.
The duration of the flight is 2 hours. We wait either in the car or back in the hanger with the team, but return to the runaway just before landing.
Just as the plane reaches the start of the runway, the mobile pilot hits the gas, swerving in from the side and then pulls under the aircraft, which comes down in just front of us.

## Slide 13
13
Notes: The mobile pilot’s job is to provide guidance to the ER-2 pilot because the plane is an awkward craft to maneuver, especially with the limited visibility afforded by the spacesuit.
To keep up with the plane, the mobile pilot rapidly accelerates to triple digit speeds, one hand on the wheel, one hand on the radio talking to the pilot in the plane.
Did I mention that the driver is a jet pilot? Trust me. Afterwards, I didn't need coffee for the 3 AM post-flight pilot debrief.
But, independent of my adrenaline level, the entire team, was very excited to see the results.

## Slide 14
Air-LUSI
Initial Results
14

## Slide 15
Air-LUSI
Initial Error Budget

## Slide 16
MODTRAN setup:
  slant path to space from 21.215 km altitude, zenith angle = 22.047°
  1976 US Standard Atmosphere, 380 ppmv CO2
MODTRAN atmospheric transmission for Air-LUSI flight 1
O2
Air-LUSI
Initial Error Budget
16

## Slide 17
The exo-atmospheric lunar spectral irradiance ELUSI is computed by dividing the at-sensor lunar spectral irradiance by the transmission Ts as a function of λ. The relative uncertainty is RSS with the at-sensor uncertainty of the transmittance.
Error propagation for atmospheric correction:
≈ 0.20% @λ = 400 nm
≈ 0.32% @λ = 620 nm
Assuming a conservative 10% error in the model, maxima are given at the following wavelengths, which has a nearly insignificant impact on the at-sensor uncertainty.
Air-LUSI
Initial Error Budget
17

## Slide 18
Air-LUSI
Results & Status
18

## Slide 19
air-LUSI Team (Left to Right) – Steven Grantham, Andrew Newton, Kevin Turpie, John Woodward, Tom Larason, Stephen Maxwell (not shown: Steve Brown, Andrew Gadsden, Andrew Cataford, and Tom Stone)
Air-LUSI
Thank You!
19