## Slide 1
MODIS/VIIRS L1B Product Status
MODIS Characterization Support Team, NASA GSFC
VIIRS Characterization Support Team, NASA GSFC
(presented by Xu Geng)
MODIS/VIIRS Calibration Workshop (May 1, 2023)
Notes: 1

## Slide 2: MODIS L1B Data Product Status
Versions in operation
  Collection 6.1: Terra V6.2.2; Aqua V6.2.3
Collection 6 discontinued in April 2023
Aqua C6.1 update to V6.2.3 in forward processing to address the increasing PV LWIR crosstalk effect after the safe-mode in March 2022
      The forward processing started on 7/27/2022
      The reprocessing between the safe mode and 7/27/2022 was completed in Nov. 2022
Terra MODIS C6.1 partial reprocess after recovery from anomaly
      CP/FP Reset – March 2022 (2022075 onwards)
      CEMs – Oct 2022 (2022296.2200 onwards)
C7 L1B code/LUT are undergoing science testing
1st set of code/LUT delivered in March 2021 with subsequent improvements.
C7 L1B reprocess is expected in Spring of 2024
Started merging C7 RSB calibration algorithm to C6.1 forward production (03/2023)
  Phase-in period: Aqua – 3 months; Terra – 10+ months

## Slide 3: MODIS L1B Production Timeline (C6 & C6.1)
Year
2012
2013
2014
2015
2016
2017
2018
Terra Forward Processing
Collection 6.1
Aqua Forward Processing
LUT Versions
Code Versions
LUT Versions
Code Versions
Production Start
Production Start
2019
2020
2021
2022
0-86
2023
Collection 6
6.1.17 (2012200)
1, 2, 4-29
6.1.14 (2012310)
1-29
6.1.16 (2014206)
6.1.31 (2014226)
2-6
3-8
6.1.18 (2014358)
1-8
6.1.33 (2015014)
6.2.2 (2017244)
6.1.20 (2015136)
1-20, 22-23, 25-31
6.1.35 (2015163)
1-11, 13-29
2024
0-74
6.1.37 (2017132)
6.1.26 (2017132)
0-85
0-88
6.2.1 (2017244)
6.2.3 (2022208)
0-12

## Slide 4: C6 and C6.1 L1B LUT Updates
 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Terra C6 | 5 | 14 | 17 | 18 | 14 | 14 | 14 | 15 | 14 | 14 | 18 | 2
Terra C6.1 |  |  |  |  |  | 10 | 13 | 13 | 16 | 13 | 18 | 4
Terra OBPG |  | 1 | 15 | 17 | 3 |  |  |  |  |  |  | 
Aqua C6 | 7 | 11 | 15 | 16 | 16 | 13 | 16 | 14 | 14 | 16 | 17 | 2
Aqua C6.1 |  |  |  |  |  | 6 | 16 | 14 | 13 | 16 | 18 | 4
Aqua (OBPG) | 1 | 9 | 13 | 13 | 13 | 13 |  |  |  |  | 6* | 4*
Total | 13 | 35 | 60 | 64 | 46 | 56 | 59 | 56 | 57 | 59 | 77 | 16
* Upon OBPG’s request without including the PV LWIR xtalk correction

## Slide 5: Collection 7 L1B Major Changes
Implemented the crosstalk correction algorithm to all detectors in PV LWIR bands and select detectors in MWIR bands.
Implemented edge correction to address the absence of sending band data for pixels at the scan edges in PC, PV LWIR and MWIR xtalk corrections.
Various Calibration algorithm improvements reflected in C7 LUT
Integrated with C7 API developed by LDOPE to facilitate the transition to NetCDF4/HDF5
The technical memos summarizing the code changes and algorithm enhancements can be found from,
  https://mcst.gsfc.nasa.gov/content/collection-7

## Slide 6: VIIRS L1B Data Product Status
    VIIRS L1 software/LUT and data design are developed under NASA EDOS/SIPS.
    L1 software maintained by NASA Ocean group
    VCST provide LUT updates as well as software development support
    S-NPP L1B C2 is ongoing at Land SIPS – LSIPS Archive Set 5200 using L1B software V3.1
    S-NPP L1B C1 is ongoing at Land SIPS for Level-2 downstream process. LSIPS Archive Set 5000 (using SDR Mx software and LUT) and 5110 (using L1B software V2.0).
    NOAA-20 (JPSS-1) C2.1 is ongoing – LSIPS Archive SET 5201 using L1B software V3.1.
    NOAA-21 (JPSS-2) L1B is ongoing – LSIPS Archive SET 4014 (not publicly available) using L1B software V3.2 (released in Nov 2022) and VCST LUT. On-orbit L1B LUTs have been delivered to SIPS for ongoing Cal/Val.
    Future Improvements (ongoing work):
    Roll over algorithm in calibration and quality flag in L1B.
    Uncertainty algorithm to be applied in L1B.
    Move the hard-coded dynamic range parameters to a LUT
    Change the DeltaC LUT from static to dynamic

## Slide 7
VIIRS S-NPP L1B Products (SIPS Support)
NASA SIPS L1B Products for S-NPP (6-min granule in NetCDF format)
  Calibrated data files are reduced from 22,000 SDRs to 720 L1Bs daily.
  First L1B software V1.1.0 was released in Jan 2016.
  Software V2.0.0 was released in Oct 2016.
  Software V3.0.0 was released in August 2018 for both S-NPP and NOAA-20 (JPSS-1).
  Software V3.1.0 was released in October 2020.
Page 7

## Slide 8
VIIRS SDR Products (S-NPP only) (SIPS Support)
Land SIPS SDR process using modified IDPS Code with VCST LUTs (C1.0 and C1.1)
  Modified IDPS SDR/EDR codes Mx based version with LUTs input from VCST.
  Total of 102 sets of LUTs for RSB and DNB have been delivered to Land SIPS for data reprocessing and SDR/EDR assessments in Collections 1.0 and 1.1.
Page 8

## Slide 9
VIIRS N20 (JPSS1) L1B Products (SIPS Support)
NASA SIPS L1B Products for NOAA-20 (JPSS-1)
  L1B software V3.0.0 was released in August 2018 with full S-NPP and JPSS-1 support.
  V3.0.0 LUTs updates are being released by VCST with 2 months forward prediction.
  Land SIPS started JPSS-1 mission reprocessing Collection 2 using V3.0.0 software in June 2019 and completed in September 2019.
  L1B software V3.1.0 was released in October 2020 for Collection 2.1 reprocessing; forward process ongoing.
Page 9

## Slide 10
Page 10
NASA SIPS L1B for JPSS-2 VIIRS
  L1B software V3.2.3 was released in November 2022 with JPSS-2 support available at Ocean group GIT for J2 VIIRS processing .
  J2 pre-launch calibration look-up-tables LUT (NetCDF format ) was delivered to NASA SIPS in October 2022 for systems testing and integration.
  The first J2 on-orbit L1B LUT was delivered in December 2022 prior to nadir aperture door opening.
  LUT V3.2.3.5 contains mission update and can be used for reprocessing
  VCST continues updating L1B LUTs derived from on-board calibrators observation and analysis.
VIIRS N21 (JPSS2) L1B Products (SIPS Support)

## Slide 11: Summary
Terra and Aqua MODIS continue to operate normally
  MODIS C6 discontinued in April 2023, C6.1 is the primary product, and C7 is undergoing science testing
  Gradually phase-in C7 RSB calibration algorithms to C6.1 forward production
SNPP, N20 (J1), and N21(J2) VIIRS also continue to operate normally
  C2 (SNPP) and C2.1 (N20) are the primary products.
JPSS-2 VIIRS on-orbit LUTs update undergoing
Dedicated efforts have been made by the MCST and VCST
Characterize on-orbit sensor performance
Evaluate and address issues identified, including cross-sensor calibration differences (critical to consistent and long-term data records)
Support science data production and reprocessing