## Slide 1
SNPP, NOAA20 and 21 VIIRS RSB calibration performance and inter-comparison assessment
VIIRS Characterization Support Team, NASA GSFC
(presented by Aisheng Wu)
MODIS and VIIRS Calibration Workshop, College Park, MD, May 1, 2023

## Slide 2
Introduction
Methodology
  Vicarious approaches (SNO, desert, Dome C and DCC)
  Data: NASA SLIPS C2 L1B for SNPP and NOAA21
Results
  Stability and inter-comparison
Summary
VIIRS RSB |  | 
Band | CW (nm) | BW (nm)
M1 | 412 | 20
M2 | 445 | 18
M3 | 488 | 20
M4 | 555 | 20
M5 | 672 | 20
M6 | 746 | 15
M7 | 865 | 39
M8 | 1240 | 20
M9 | 1378 | 15
M10 | 1610 | 60
M11 | 2250 | 50
I1 | 640 | 80
I2 | 865 | 39
I3 | 1610 | 60

## Slide 3
3
Pseudo-Invariant Calibration Sites (PICS):
  PICS approaches include desert (Libya 4) and Dome C
  Near-nadir, 16-day repeatable orbits for Libya-4, daily overpasses for Dome C in Antarctic summer.
  Target area of 25 x 25 km. Employ semi-empirical (desert) and empirical (Dome C) BRDF correction. BRDF coefficients derived initial years of on-orbit measurements
  DCC approach
  DCC pixels collected over western tropical Pacific. Mu et al. "Optimization of a Deep Convective Cloud Technique in Evaluating the Long-Term Radiometric Stability of MODIS Reflective Solar Bands", Remote Sensing, vol. 9 (6), issue 535, 2017.
  Impact due to RSR differences: Correction applied based on SBAF derived using historic SCIAMACHY hyperspectral data
Libya 4
Dome C
25 x 25 km
Vicarious approaches

## Slide 4
Simultaneous Nadir Overpasses (SNO)
  Aqua MODIS used as a transfer radiometer for SNPP, NOAA20/21 intercomparison. TOA reflectance ratio between VIIRS/MODIS from high-latitude SNO (<3 minutes, two-line element), one SNO every 3-4 days
  No BRDF correction applied
  Correction for RSR mismatch based on a scene-averaged SCIAMACHY hyperspectral profile over typical high-latitude
  Larger uncertainties in some SWIR bands (compared to the VIS/NIR bands) likely due to their high sensitivity to atmospheric conditions
Pixel-by-pixel match from SNO on Oct 8, 2019
Vicarious approaches

## Slide 5
Spectral band adjustment factor (SBAF)*
Band | M1 | M2 | M3 | M4 | M5 | M7 | I1 | I2 | M8 | M10 | I3
Desert | 0.9966 | 0.9987 | 0.9995 | 0.9933 | 1.0073 | 0.9957 | 0.9983 | 0.999 | 0.9892 | 0.9925 | 0.9947
Snow | 0.9974 | 0.9999 | 1.0009 | 1.0018 | 1.0009 | 0.9923 | 1.0001 | 0.9988 | 1.0029 | N/A** | N/A
Ocean | 0.9969 | 0.9987 | 1.0033 | 1.008 | 0.9901 | 0.9902 | 1.0056 | 0.9959 | 0.9997 | N/A | N/A
Cloud | 0.9974 | 0.9996 | 1.0011 | 1.0043 | 1.0034 | 0.9954 | 0.9986 | 0.999 | 0.9944 | 0.9787 | 0.9763
*The SBAF correction is determined using historic hyperspectral observations from SCIAMACHY, one of ten instruments aboard of ESA's Environmental Satellite, ENVISAT
** Large variations (>3%) in SBAF for different scene types
SBAF between NOAA20 and 21 RSB

## Slide 6
Reflectance trends over desert site
SNPP-based BRDF applied to both sensors
6

## Slide 7
Reflectance ratio trends (VIIRS/Aqua MODIS)
7

## Slide 8
Reflectance trends over DCC
8

## Slide 9
Reflectance trends over Dome C
SNPP-based BRDF applied to both sensors
9

## Slide 10
Band (µm) | M1 0.41 | M2 0.45 | M3 0.49 | M4 0.56 | M5 0.67 | M7 0.87 | M8 1.24 | M9 1.38 | M10 1.61 | M11 2.25 | I1 0.64 | I2 0.87 | I3 1.61
Libya4 | 7.5 1.0 | 6.3 1.6 | 4.4 0.0 | 3.3 2.1 | 4.5 -1.7 | 2.7 -0.3 | 2.4 0.9 |  | 1.8 3.1 | 1.7 2.3 | 2.9 -1.1 | 2.6 -1.0 | 3.0 0.5
DCC | 6.7 1.3 | 5.3 1.6 | 5.6 2.5 | 6.8 -0.4 | 5.0 -0.1 | 4.8 0.8 | 1.8 4.3 | 0.6 7.4 | 0.3 0.4 | 1.9 5.5 | 4.4 -0.3 | 5.4 0.4 | 2.5 -0.5
Dome C | 8.3 2.1 | 6.7 2.4 | 5.0 0.9 | 4.7 0.1 | 5.1 2.0 | 2.4 0.9 |  |  |  |  | 3.3 0.9 | 2.6 1.2 | 
Aqua SNO | 6.6 1.2 | 5.9 1.7 | 4.3 1.6 | 5.2 0.6 | 4.9 -0.3 | 3.2 0.8 | 2.9 0.9 |  | 3.0 1.7 | 4.6 5.1 | 3.2 0.9 | 3.0 0.8 | 3.9 1.2
SNPP, NOAA20 and NOAA21 VIIRS RSB comparison
*Results from NOAA21 VIIRS are preliminary based on Libya 4, Dome C and SNO approaches
RSR correction for NOAA21 is based on those from NOAA20
SNPP-NOAA20 (black), NOAA20-NOAA21 (red), Results provided in percentage (%)
10

## Slide 11
11
Assessment of calibration consistency among SNPP, NOAA20 and 21 VIIRS RSB is based on vicarious approaches (SNO, desert, Dome C and DCC)
While SNPP and NOAA20 have a stability within 2% over the mission, it shows that the NOAA20 reflectances are systematically lower than SNPP by about 4 to 7% for bands M1 to M3 (shortest wavelengths) and 2-4% for the rest bands.
Initial comparison shows that the NOAA21 VIIRS reflectances are consistent with NOAA20 to within 2% for VIS/NIR. Impacts of the spectral differences based the SBAF analysis indicate they are within 0.5% (VIS/NIR) for most scene types. For SWIR bands, large inconsistent (>5%) results are observed.
Comparison results indicate that agreement among the different approaches are up to 2.0%, indicating errors due to limitation of each approach.
Summary