## Slide 1: NPP and NOAA-20 VIIRS RSB radiometric scaling utilizing multiple approaches
David Doelling, Rajendra Bhatt, Conor Haney, Benjamin Scarino, Prathana Khakurel, and Arun Gopalan
CERES Imager and Geostationary Calibration Group
May 1, 2023
MODIS/VIIRS Calibration Workshop

## Slide 2: Outline
Background
  CERES EBAF flux product requirements
  CERES Imager and Geostationary Calibration Group
Radiometric scaling of VIIRS instruments
  Methods:
    All-sky tropical ocean ray-matching (ATO-RM) Aqua-MODIS/VIIRS
    Polar SNO with Aqua-MODIS/VIIRS
    PICS approach (Libya-4)
    Deep-convective clouds invariant target approach
  Spectral differences and SBAF
Results
Conclusions

## Slide 3: CERES EBAF product
The CERES EBAF monthly product provides observed broadband fluxes needed to monitor the Earth’s energy balance and validate climate models
The stability of the EBAF fluxes relies on the
  The CERES onboard calibration systems
  The well-maintained sun-synchronous orbits
  The cloud retrieval continuity between MODIS and VIIRS imagers designed to identify the angular directional model (ADMs) scene types to convert CERES observed radiances into fluxes
  The diurnal models to estimate the regional flux variability between CERES measurements, which are a combination of geostationary derived broadband fluxes and constant meteorology models
The CERES EBAF product has transitioned from Terra and Aqua inputs to a N20 only input beginning with the data month of April 2022
  The Terra and Aqua orbits have drifted outside of their mean local time window
  The Aqua spacecraft anomaly accelerated the transition
  The seamless transition was accomplished using regional climatology adjustment factors based on the 5-year Terra and Aqua overlap period that adjusts for the Terra morning observations and the MODIS and VIIRS cloud property induced flux differences

## Slide 4: CERES EBAF product
CERES utilizes their own cloud retrieval algorithm designed to minimize the number pixels with unretrieved cloud properties identified by the cloud mask
MODIS and VIIRS cloud retrieval continuity requires
  MODIS and VIIRS on orbit calibration stability
  Consistent MODIS and VIIRS analogous channel calibration
  Accounting for spectral band differences
  Using MODIS and VIIRS channels common to both
  Accounting for MODIS and VIIRS pixel size differences
CERES incorporates 22 geostationary imager derived clouds and fluxes
  The GEO channel radiances are scaled to the Aqua-MODIS C6.1 calibration reference to retrieve GEO clouds consistent the MODIS
  The GEO derived fluxes are carefully normalized to the CERES observed fluxes to estimate the regional diurnal flux using the same ADMs

## Slide 5: CERES imager and geostationary calibration group (IGCG)
The group performs calibration assessment of MODIS, VIIRS, and GEO imagers in real-time using multiple approaches
The calibration group provides the GEO visible radiometric scaling factors referenced to the MODIS C6.1 calibration metric for CERES Edition 4 products (MODIS C7 for Edition 5)
Three independent reflective solar bands (RSB) cross-calibration approaches are used to estimate radiometric SNPP and NOAA-20 VIIRS biases
  All-sky tropical ocean ray-matching (ATO-RM) between Aqua-MODIS and VIIRS
  DCC invariant target
  Pseudo-invariant ground site (Libya-4 PICS)
Datasets used are
  Aqua-MODIS Collection 6.1 level 1B product
  SNPP VIIRS V2 and NOAA-20 VIIRS V2.1 datasets generated by the NASA VIIRS Land Science Investigator-led Processing System (Land SIPS).

## Slide 6: Ray-matching with Aqua-MODIS
Coincident, co-located, and co-angled radiance pairs for all comparable channels of Aqua-MODIS and SNPP/NOAA-20 VIIRS are acquired between 30 °N and 30 °S.
Ray-matching is performed over all-sky tropical ocean (ATO-RM) scenes
  pixels averaged within a shared 50-km diameter constitutes one ray-matched radiance pair
  VZA/SZA differences < 3°, RAZ difference <10°
A linear regression forced through zero is fitted to the radiance pairs on a monthly basis and the forced-slope is used as the cross-calibration ratio.
NOAA-20 VIIRS M5
radiances are darker
compared to SNPP-VIIRS
Tropical SNO, Jan 14, 2020

## Slide 7: Ray-matching with Aqua-MODIS
Polar SNO, Apr 12, 2023
North Pole, 2021_07
South Pole, 2021_12
Aqua/N20 ratio = 1.040
Aqua/N20 ratio = 1.036
Coincident, co-located, and co-angled radiance pairs for all comparable channels of Aqua-MODIS and SNPP/NOAA-20 VIIRS are acquired poleward of 60° across all surface types.
Other wise same as ATO-RM approach

## Slide 8: Ray-matching with Aqua-MODIS
Aqua/N20 mean ratio = 1.038
All-sky Tropical Ocean, 2018-2022
Aqua/N20 mean ratio = 1.035
Poles, 2018-2022

## Slide 9: Libya4 Directional Models
Libya-4 PICS (28.6°N, 23.4°E, 0.5°x0.5°) VZA observations < 35°are considered
Libya TOA reflectance is modeled as a function of SZA (2nd order regression) and with atmospheric parameters
  Libya-4 SZA directional models (DM) stratified by back and forward scattering and by VZA
  Ozone, PW, Wind Speed, Surface pressure
DM predict the TOA reflectance to monitor the sensor stability
Sensor pair reflectance ratios are computed from the DMs using the mean conditions of Libya-4
  SZA= 28.0°, Ozone=292 DOB, PW=1.74 cm, WS=3.9 m/s, Psurf 1003.2 hpa
showing the 7 DM
DM reflectances

## Slide 10: Comparison of Libya-4 1.24µm stability with and without atmospheric parameters
N20-VIIRS
Aqua-MODIS
Before atmospheric correction
After atmospheric correction
33% sigma reduction for N20 utilizing atmospheric correction
21% sigma reduction for Aqua utilizing atmospheric correction

## Slide 11
SAT/BANDS |  | 0.64 (%) | 0.87 (%) | 0.46 (%) | 0.55 (%) | 1.24 (%) | 1.629 (%) | 2.10 (%) | (%) | (%)
Aqua | SZA+ | 0.8328 | 0.873 | 0.9791 | 0.8999 | 0.7791 | 0.657 | 1.793 |  | 
 | SZA++atm par | 0.7031 | 0.6578 | 0.9542 | 0.8346 | 0.617 | 0.6323 | 0.9144 |  | 
 |  | 15.6 | 24.7 | 2.5 | 7.3 | 20.9 | 3.8 | 49 |  | 
Terra | SZA+ | 0.8997 | 0.9887 | 1.193 | 0.9728 | 0.979 | 0.6538 | 2.0208 |  | 
 | SZA++atm par | 0.7832 | 0.7384 | 1.1724 | 0.928 | 0.8656 | 0.6198 | 1.1937 |  | 
 |  | 13.01 | 25.43 | 2.03 | 4.75 | 12.40 | 5.43 | 40.90 |  | 
SAT/BANDS |  | 0.67 (M5) | 0.87 (M7) | 0.49 (M3) | 0.55 (M4) | 1.24 (M8) | 1.629 (M10) | 2.10 (M11) | 0.64 (I1) | 1.61 (I3)
N20 | SZA+ | 0.6741 | 0.6487 | 0.9682 | 0.8688 | 0.9048 | 0.5673 | 1.5368 | 0.8442 | 0.6506
 | SZA++atm par | 0.612 | 0.5688 | 0.8791 | 0.7849 | 0.6067 | 0.5084 | 0.8286 | 0.7466 | 0.5876
 |  | 9.21 | 12.32 | 9.20 | 9.66 | 32.95 | 10.38 | 46.08 | 11.56 | 9.68
NPP | SZA+ | 0.6072 | 0.6733 | 0.8817 | 0.8146 | 0.8809 | 0.5381 | 1.5139 | 0.7203 | 0.5412
 | SZA++atm par | 0.5448 | 0.5403 | 0.7912 | 0.7079 | 0.5736 | 0.4859 | 0.8083 | 0.6001 | 0.4906
 |  | 10.27 | 19.75 | 10.26 | 13.09 | 34.88 | 9.70 | 46.60 | 16.69 | 9.34
SAT/BANDS |  | 0.64 (%) | 0.87 (%) | 0.46 (%) | 0.55 (%) | 1.24 (%) | 1.629 (%) | 2.10 (%) | (%) | (%)
Aqua |  | 0.8328 | 0.873 | 0.9791 | 0.8999 | 0.7791 | 0.657 | 1.793 |  | 
 |  | 0.7031 | 0.6578 | 0.9542 | 0.8346 | 0.617 | 0.6323 | 0.9144 |  | 
 |  | 15.6 | 24.7 | 2.5 | 7.3 | 20.9 | 3.8 | 49 |  | 
Terra |  | 0.8997 | 0.9887 | 1.193 | 0.9728 | 0.979 | 0.6538 | 2.0208 |  | 
 |  | 0.7832 | 0.7384 | 1.1724 | 0.928 | 0.8656 | 0.6198 | 1.1937 |  | 
 |  | 13.01 | 25.43 | 2.03 | 4.75 | 12.40 | 5.43 | 40.90 |  | 
SAT/BANDS |  | 0.67 (M5) | 0.87 (M7) | 0.49 (M3) | 0.55 (M4) | 1.24 (M8) | 1.629 (M10) | 2.10 (M11) | 0.64 (I1) | 1.61 (I3)
N20 |  | 0.6741 | 0.6487 | 0.9682 | 0.8688 | 0.9048 | 0.5673 | 1.5368 | 0.8442 | 0.6506
 |  | 0.612 | 0.5688 | 0.8791 | 0.7849 | 0.6067 | 0.5084 | 0.8286 | 0.7466 | 0.5876
 |  | 9.21 | 12.32 | 9.20 | 9.66 | 32.95 | 10.38 | 46.08 | 11.56 | 9.68
NPP |  | 0.6072 | 0.6733 | 0.8817 | 0.8146 | 0.8809 | 0.5381 | 1.5139 | 0.7203 | 0.5412
 |  | 0.5448 | 0.5403 | 0.7912 | 0.7079 | 0.5736 | 0.4859 | 0.8083 | 0.6001 | 0.4906
 |  | 10.27 | 19.75 | 10.26 | 13.09 | 34.88 | 9.70 | 46.60 | 16.69 | 9.34
monthly Libya-4 reflectance linear regression standard errors in (%)
The Libya-4 reflectance is correlated with SZA + SZA2 + Ozone, PW, Wind Speed, Surface pressure
The red values represent the reduction of the standard error by using atmospheric parameters
PW was the dominant atmospheric parameter
Libya-4 temporal stability table

## Slide 12: Baseline DCC method
DCC pixel selection criteria:
  BT11μm < 205.0°K, SZA < 40°, VZA < 40°, 10° < RAA < 170°, σ(BT11μm) < 1.0° K, and σ(VIS) <3%
DCC pixels are compiled into monthly probability distribution functions (PDFs) and their modes are tracked over time.
Anisotropic correction using the angular distribution model by Hu et al [3].
Suitable for wavelengths <1 μm
At SWIR wavelengths,
  DCC reflectivity is affected by ice particle size
  larger ice particles are more absorbing
  results in large seasonal cycles
  DCC response is highly dependent on the IR BT threshold
DCC radiance (M5)
Frequency
Frequency
SNPP-VIIRS
NOAA-20 VIIRS

## Slide 13: Improved DCCT for SWIR bands
Proper seasonal characterization of DCC allows the extension of DCC method to calibrate SWIR channels.
Channel-specific BRDFs are constructed using the SNPP-VIIRS DCC samples from 2012-2016
Pixel-level DCC reflectance values are partitioned into angular bins
  Angular discretization:
    VZA and SZA range from 0-55° with a 5° step size
    RAA varies from 0-180° at 10° intervals
VIS-NIR BRDFs are similar to Hu model
Cirrus Channel (1.38 μm)
  Ground PICS are inapplicable for vicarious calibration
  Radiation is mostly absorbed by atmosphere, except in the case of high-altitude ice clouds
SWIR band BRDFs reduces temporal variability of DCC response by up to 65%.
By implementing similar DCC thresholds and BRDF normalizations, inter-sensor comparison using mean and mode statistics is feasible.

## Slide 14: Radiance and Reflectance biases
Reference Solar Spectrum | Impact on M4 band calibration
VIIRS instruments are calibrated on Reflectance scale SNPP and NOAA-20 VIIRS use different solar irradiance models Biases are different for radiance and reflectance Difference in reference solar spectra can induce additional (+/-) radiance bias | 
Reference Solar Spectrum | Impact on M4 band calibration
Solar constant tool: https://cloudsway2.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SOLAR-CONSTANT-COMPARISONS
~2% difference in Esun for M4 (0.55 µm) band
SNPP-VIIRS
NOAA-20 VIIRS

## Slide 15: SRF differences and SBAF
SRFs are similar for most of the bands
SBAF correction are within 2% for all scene types
SCIAMACHY-based SBAF
M4 channel
ATO scene
Hyperion-based SBAF
M11 channel (2.25µm)
Libya-4

## Slide 16: N20/SNPP reflectance ratios
M3
M4
M5
M9
M8
M7

## Slide 17: N20/SNPP reflectance ratios
M10
M11
I1
I3

## Slide 18: NPP-N20 Bias Table
Reflectance biases are provided in parenthesis
‘+’ indicates SNPP-VIIRS is brighter
Band | Radiometric bias 100% x (1-NOAA-20/SNPP) |  |  |  | 
 | Aqua-MODIS ATO-RM | Aqua-MODIS DCC-RM | Libya-4 PICS | DCC IT | Approach consistency
M3 (0.48µm) | 5.5 | 5.4 | 5.4 | 5.2 | 0.3
M4 (0.55µm) | 5.6 | 5.5 | 4.9 | 5.4 | 0.7
M5 (0.65µm) | 5.3 | 5.1 | 4.6 | 5.0 | 0.7
I1 (0.65µm) | 4.5 | 4.6 | 4.4 | 4.7 | 0.3
M7 (0.86µm) | 4.0 |  | 4.2 | 3.9 | 0.3
M8 (1.24µm) | 2.1 | 1.7 | 2.1 | 1.8 | 0.4
M9 (1.38µm) |  | 1.2 |  | 1.1 | 0.1
M10 (1.6µm) | 2.9 | 2.8 | 1.9 | 2.5 | 1.0
I3 (1.6µm) | 4.4 | 4.7 | 4.9 | 5.0 | 0.6
M11 (2.25µm) |  |  | 1.3 | 1.9 | 0.7
I1 bias from multiple approaches are more consistent than M5, since I1 and B1 SRFs are more similar

## Slide 19: NPP-N20 Bias Table (%)
Band | CERES-Libya | MAIAC | CERES combined | VCST
M3 | 5.4 | 4.8 | 5.6 | 4.8
M4 | 4.9 | 5.5 | 5.8 | 4.5
M5 | 4.6 | 4.4 | 5.4 | 4.4
M7 | 4.2 | 3.8 | 4.2 | 3.3
M8 | 2.1 | 2.6 | 2.0 | 2.4
M10 | 2.5 | 2.2 | 2.5 | 0.9
M11 | 1.3 | 2.0 | 1.6 | 1.7
I1 | 4.4 | 4.0 | 4.8 | 3.9
I3 | 4.9 | 5.4 | 5.0 | 3.5
CERES Libya-4 and MAIAC within 0.8%
CERES combined and MAIAC agree within 0.8%
CERES combined and VCST agree within 1.7%
Calibration of the SNPP and NOAA 20 VIIRS Sensors for Continuity of the MODIS Climate Data Records, Lyapustin et al. 2023, submitted RSE

## Slide 20: Conclusions
The CERES EBAF product relies on Terra/Aqua MODIS and SNPP/N20 VIIRS cloud retrieval continuity
The CERES imager and geostationary calibration group (IGCG) utilized ATO-RM, DCC-RM using Aqua-MODIS as a transfer radiometer, Libya-4 and DCC-IT to determine the NPP and N20 radiometric scaling factors
  All approaches were within 0.8% across all VIIRS channels
  The combined CERES approaches were within 0.8% and 1.7% of the MAIAC and VCST
Aqua-MODIS can no longer be used as transfer radiometer to determine the SNPP and N20 VIIRS RSB radiometric scaling
  The Terra and Aqua orbits are drifting outside of their mean local time windows
The CERES project will use the Libya-4 and DCC-IT as well Aqua-MODIS/VIIRS polar-RM approaches to determine the SNPP and N20 VIIRS RSB radiometric scaling