## Slide 1: (SNPP + J1/N20 + J2/N21 + J3 + J4) VIIRS Geometric Calibration Status
NASA VIIRS Characterization Support Team (VCST)
Geometric Calibration Group
Guoqing (Gary) Lin, Robert E. Wolfe, NASA/GSFC Code 619
Ping Zhang, Bin Tan, Apexa Patel, SSAI/GSFC Code 619
John Dellomo, GST/GSFC Code 619
NASA MODIS/VIIRS Calibration Workshop
1 May 2023, In-person
(last in-person Nov 2019; last one on 25 Feb 2021, virtual)

## Slide 2: Outline
Changes since STM in Feb 2021
SNPP VIIRS Geolocation in C1.1, C2
J1/N20 VIIRS Geolocation in C2, C2.1
J2/N21 VIIRS initial Geolocation in “C2”
Expectations for J3, J4 VIIRS
Plan in future work
Conclusions
VCST/GEO 2

## Slide 3: Changes since last STM
Refreshed ground control point (GCP) chip library from Landsat-8 images, generating ~ 4X as many daily matches as in the existing GCP library
  fully utilized in SNPP C2
  J1/N20 C2.1 (in L1, but used to generate C2 in L2+ products)
  J2/N21 “C2”, test archive
SNPP C2 also implemented
  Kalman Filter for attitude improvement
  VIGMU (VIIRS instrument geometric model update)
  Temporal pointing correction
J2 launched on 11/10/2022, became NOAA-21
J3 VIIRS is in I&T with spacecraft
J4 VIIRS completed ambient tests
VCST/GEO 3

## Slide 4: GCP refresh & match improvements
1214 existing chips mostly from Landsat-7
24 x 24 km2 chip size
196 daily matches
Error search
  56 deg
  2.5 pixels
  0.85 minCCV
2514 (2.1X) new chips from Landsat-8
42 x 42 km2 chip size
841 (4.3X) daily matches
Error search
  56 deg scan angle
  2.5 pixels
  0.85 minCCV
New ground control points (GCPs) are used in SNPP C2, J1 C2.1, and J2 “C2”.
Tropic of Cancer
Tropic of Capricorn
Tropic of Cancer
Tropic of Capricorn
GCPs within tropics seasonally switch side in the satellite mornings/afternoons
The existing GCP library is still used in SNPP C1.1, and J1 C2 (L1 only)
VCST/GEO 4

## Slide 5: VIIRS Geolocation Performance
Residuals | SNPP C1.1 | SNPP C2 | J1/N20 C2 | J1/N20 C2.1 | J2/N21 “C2”
Track mean | 14 m | 2m | 2m | -4 m | -8 m
Scan mean | 5 m | 5 m | -2 m | 5 m | 2 m
Track RMSE | 59 m | 59 m | 55 m | 57 m | 60 m
Scan RMSE | 53 m | 48 m | 50 m | 47 m | 48 m
Data-days | 4081 (11.2 yrs) | 4081 (11.2 yrs) | 1917 (5.2 yrs) | 1917 (5.2 yrs) | 73 (0.2 yrs)
Missing days | 16 | 16 | 3 | 3 | 1
Daily matched GCPs w/ I1 | 199 | 845 | 194 | 838 | 846
Nadir equivalent accuracy (RMSE – Root Mean Square Error)
  Meet Spec: 125 m (1s); within 20% I1 HSI (375 m) = 75 m @ nadir
  Band-to-band mis-registration to other bands adds bias to RMSE to :
SNPP C2 uses Kalman filter for attitude improvement, VIGMU to remove oscillations in scan direction, and time-dependent instrument-to-spacecraft interface angles to remove temporal pointing variations
New chip library is used in SNPP C2 and J1/N20 C2.1 re-processing
J2/N21 data archive is currently in test archive, “C2”, and using the new chip library
VCST/GEO 5
New Chip Library

## Slide 6: SNPP C1.1 geolocation errors
VCST/GEO 6
C1.1 RMSE Track: 53 m Scan: 48 m, nadir equivalent
20% I-band pixel size
Temporal variations are corrected in C2

## Slide 7: SNPP C2 geolocation errors
VCST/GEO 7
C2 RMSE Track: 59 m Scan: 48 m, nadir equivalent
20% I-band pixel size
New Chip Library
Errors in forward-processing will be corrected in future re-processing

## Slide 8: Time series for SNPP VIIRS pointing correction
A B C D E F G H I
Events:
2012-11-22, side switch of VIIRS scan control electronics
2013-4-25, erroneous star trackers realignment
2015-8-19, 1-second time error onboard of SNPP (213 arcsec pitch error) for 7 hours
2019-3-22, Star Tracker-2 reset
2021-2-8, LUTs updates for forward processing in constant values
2021-8-3, safe hold and sun pointing
2021-11-27, Global Positioning System (GPS) had issued a "0" leap second
2022-1-13, LUTs updates for forward processing in constant values
2022-7-26, safe hold and sun pointing
These are corrected for in C2.
VCST/GEO 8

## Slide 9: SNPP scan profiles
C1.1 results (old chip lib)
C2 results (new chip lib)
Strange pattern is corrected in C2
VIGMU (VIIRS instrument geometric model update) is implemented in C2
Tilt and curvature will be corrected in the future
VCST/GEO 9

## Slide 10: J1/N20 C2.1 geolocation errors
VCST/GEO 10
C2.1 RMSE Track: 57 m Scan: 47 m, nadir equivalent
20% I-band pixel size
VCST/GEO 10
Uncorrected
Corrected for temporal variation

## Slide 11: J1/N20 C2 geolocation errors
VCST/GEO 11
C2 RMSE Track: 55 m Scan: 50 m, nadir equivalent
20% I-band pixel size
VCST/GEO 11
Pointing correction
Courtesy: https://www.star.nesdis.noaa.gov/icvs/status_N20_sc.php
Pointing variation is likely related to beta angle
Old Chip Library

## Slide 12: J1/N20 scan profiles
C2 results (old chip lib)
C2.1 results (new chip lib)
VIGMU (VIIRS instrument geometric model update) implemented in J1 C2+
VCST/GEO 12

## Slide 13: J2/N21* “C2” geolocation errors
VCST/GEO 13
“C2” RMSE Track: 61 m Scan: 48 m, nadir equivalent
20% I-band pixel size
VCST/GEO 13
After first on-orbit correction
Scan angle profiles
* J2 launched: 11/10/2022; Nadir door opened 12/5/2022; Geolocation LUTs updated 12/22/2022.
* Ka antenna transmitter failed 12/16/2022; Redundant Ka antenna activated 2/2/2023.
* J2 “C2” is currently in a test archive.
cryo door open
2/8/2023

## Slide 14: Expectations for J3, J4 VIIRS
J3 is in I&T with SC while J4 completed ambient tests
J3, J4 Geolocation – should be good with on-orbit calibration
J3, J4 Effective Focal Length (EFL) & scan period are shortened to mitigate scan-to-scan underlaps Swath width increases
VCST/GEO 14
 | EFL (mm) | Scan rate (rad/s) | Scan period T (s) | EV scan angle (deg) | EV ground distance (km)
SNPP | 1135 | 3.531 | 1.7793 | 56.28 | 1530
JPSS-1 | 1141 | 3.517 | 1.7867 | 56.04 | 1510
JPSS-2 | 1143 | 3.510 | 1.7899 | 55.94 | 1500
JPSS-3 | 1134 | 3.535 | 1.777 | 56.34 | 1535
JPSS-4 | 1131 | 3.546 | 1.772 | 56.5 | 1550
 | EFL (mm) | Scan rate (rad/s) | Scan period T (s) | EV scan angle (deg) | EV ground distance (km)
SNPP | 1135 | 3.531 | 1.7793 |  | 
JPSS-1 | 1141 | 3.517 | 1.7867 |  | 
JPSS-2 | 1143 | 3.510 | 1.7899 |  | 
JPSS-3 | 1134 | 3.535 | 1.777 |  | 
JPSS-4 | 1131 | 3.546 | 1.772 |  | 
As-built VIIRS EFLs and scan rates and EV coverages
Initial design
Mitigated
fabrication
target
, if < 0  underlap
where F = effective focal length, p = detector “pitch” interval in the track direction, n = # detectors, h = range from satellite to earth terrain surface altitude, T = scan period, i=inclination angle (in ECI) > 90 deg, VECI = spacecraft ground speed in the inertial frame, Vearth0 = speed of earth rotation at equator, Overlap < 0 indicates underlap.

## Slide 15: Scan-to-scan underlaps
Underlaps occur near 15oN, close off going north and south and off-nadir scan angles.
High terrain widens/creates the underlaps.
J2 has most of this issue
SNPP has almost none of the issue because of its shorter focal length (~0.5%).
J3, J4 mitigate the issue by shortening EFL & scan period
J1 Underlap
80m
Within scan
Inter-scan
Inter-HAM-sides
Terrain effect
, if < 0  underlap
where F = effective focal length = Mag x aft optic focal length, p = detector “pitch” interval in the track direction, n = # detectors, h = range from satellite to earth terrain surface altitude, T = scan period, i=inclination angle (in ECI) > 90 deg, VECI = spacecraft ground speed in the inertial frame, Vearth0 = speed of earth rotation at equator, Overlap < 0 indicates underlap.
VCST/GEO 15
Inter-scan
Within scan
J2 underlap
110m
Terrain effect
Within scan
Inter-scan
NPP overlap

## Slide 16: Future work
Routine monitor and LUTs update as needed
Update LWM (year by year)
Create GCST (Geometric Characterization Support Team) website
Create ground control point chip library in multi-spectral bands and implement in geolocation monitoring system (Landsat-8 band B6 chips available now for VIIRS band I3 geolocation error detection)
Update DEM from 1 km to 500m or finer resolution
Refine LUTs to correct for scan angle dependent biases
Replace SNPP and J1 ephemeris in SC diary with GPS data
Automate GEO LUT updates
Anything else?
Any change in priority order?
VCST/GEO 16

## Slide 17: Conclusions
SNPP VIIRS geolocation performance is good
  Mean errors for I- & M-bands are ~ 10 m and uncertainties @1-s are ~ 60 m at nadir, statistically.
  C2 perform better after implementing: 1) Kalman Filter for attitude; 2) VIGMU (VIIRS instrument geometric model update); 3) temporal pointing correction; 4) new GCP library.
J1/N20 VIIRS geolocation performance is good
J2/N21 VIIRS initial on-orbit geolocation is good
J3 VIIRS is being integrated with SC and J4 VIIRS completed ambient tests
  Shorter EFL and scan period mitigate scan-to-scan underlaps
VCST/GEO 17

## Slide 18
Local arithmetic mean Local Stdev
Global arithmetic mean ,
Global Stdev
Root-mean-square-error (1-s)
3-s error bound
Some short-term anomalous Ak , may be buried in long-term A, S.
Questions?
Thank you !
VCST/GEO 18

## Slide 19: Backup Slides
VCST/GEO 19

## Slide 20: VIGMU: VIIRS instrument geometric model update
Puzzle: ground geolocation SW is supposed to correct RTA/HAM motion non-linearity
Long term trend from SNPP VIIRS still shows the pattern, but in the opposite direction
Answer:
Lsight = Ltel - 1/M ( Ltel – Lhamvector)
where M = -4 (not +4 as we are currently using), which affects line of sight due to the parts of RTA/HAM motion non-linearity (non-synchronization), which are relatively small

## Slide 21: SNPP Attitude control & knowledge errors 2016-05-02 06:48:50 – 06:50:40z
Western Australian coast (south up)
Difference in “land”/”Water” masks from data 16 days earlier
with correction
Knowledge error
Control (to 0) error
0 line

## Slide 22: SNPP SC attitude performance - - Spec outage and trend
Large circles for control spec outage; Small dots hint knowledge spec outage
Star tracker cooling improved SNPP attitude performance
We are seeking for further improvements1
SW with Kalman filter to refine the attitude for NASA SIPSs is implemented in C2
J1 is performing better
1. My eRooms > S-NPP Flight Operations and Support > FARB > All Discussion Topics--Artifacts and Minutes > DR 6348--SNPP STAR TRACKER DEGRADATIONS OVER MISSION LIFE: ATTITUDE EXCURSIONS AND LUNAR INTRUSIONS > SNPP ADCS and Geolocation Report
using ~90% data
VCST/GEO 22

## Slide 23: Sun angle dependence
SNPP C1.1 (old chip lib)
SNPP C2 (new chip lib)
VCST/GEO 23

## Slide 24: Sun angle dependence
J1/N20 C2 (old chip lib)
VCST/GEO 24
J1/N20 C2.1 (new chip lib)

## Slide 25: J2 VIIRS Scan-to-scan underlaps
overlap
underlap
underlap
Within scan
Inter-scan
Inter-scan
Widest underlaps occur at nadir near 15oN at ~100 m in this case. They narrow down as N21 goes north or south due to increasing altitude.
High terrain widens the underlaps.
N20 VIIRS has smaller underlap (next chart)
SNPP VIIRS has less of this issue because of its shorter focal length and faster scan speed (~0.5%) than N20 VIIRS
Terrain effects
2023-02-10 19:30z - 20:20z
VCST/GEO 25

## Slide 26: J1 VIIRS Scan-to-scan underlaps
Widest underlaps occur at nadir near 15N at ~ 70 m in this case. They narrow down as J1 goes north or south due to increasing altitude. They also close in off nadir angles (@ ~10 deg) due to bowtie effects
High terrain widens the underlaps.
SNPP VIIRS has less of this issue because of its shorter focal length and faster scan speed (~0.5%)
Underlap
overlap
Underlap
Within scan
Inter-scan
Inter-HAM-sides
Terrain effects
where F = effective focal length = Mag x aft optic focal length, p = detector “pitch” interval in the track direction, n = # detectors, h = altitude, T = scan period, i=inclination angle (in ECI) < 90 deg for J1, VECI = spacecraft ground speed in the inertial frame, Vearth0 = speed of earth rotation at equator, Overlap < 0 indicates underlap.
, if < 0  underlap
VCST/GEO 26

## Slide 27: SNPP C1 NRT as5000 geolocation errors
VCST/GEO 27
C1 RMSE Track: 51 m Scan: 46 m, nadir equivalent minCCV=0.90
20% I-band pixel size
Temporal variations are corrected in C2